## Slide 1: ATF2: Accelerator Test facility
A.Jeremie
LAPP: A.Jeremie
LAL: P.Bambade, Shan Liu , S.Wallon, F.Bogard, O.Blanco, P.Cornebise, I. Khvastunov, V. Kubytskyi
And fruitful work with KEK, KNU, IFIC, IHEP, UK and CERN colleagues (not listed)

## Slide 2: What was done by the French teams around ATF2
Introduction
Vibrations and GM feedforward
IP-BPM and chamber
Beam-halo evaluation : diamond sensor
Conclusion Outlook

## Slide 3
Goal 1: 37 nm beam at the focal point in a stable and reproducible manner
Goal 2: Stable trajectory (D<2nm) and ILC-like intra-train feedback
Shintake monitor

## Slide 4
“Routinely” produce 45 nm beams at ATF2!
Modulation of photon rate by Compton diffusion on interference fringes
Focused beam
Less focused
Shintake Monitor: essential for beam tuning
44nm beam size: Already a record!
Big step towards ILC feasibility!

## Slide 5: What was done by the French teams around ATF2
Introduction
Vibrations and GM feedforward
IP-BPM and chamber
Beam-halo evaluation : diamond sensor
Conclusion Outlook

## Slide 6
14 Guralp 6T sensors all along ATF2
Guralp 6T: 0,5Hz-100Hz, two directions connected (vertical and horizontal can be placed parallel or perpendicular to beam direction), mainly in Extraction line, 2 sensors easily relocated

## Slide 7: What magnets need studying?
IP
The most sensitive magnet is QD0FF, then comes QF1FF (which was recently changed and needs to be studied) then QD10FF pair
QD0FF
QF1FF
QD10FF pair
Tolerance (vertical) | QD0FF | QF1FF (old support and magnet) | QF1FF (new magnet and support)
7 nm (QD0) 20 nm (QF1) | 4.8 nm | 6.3 nm | 30nm

## Slide 8: Relative displacement at 1Hz
QD10FF/floor | Vertical (nm) | Horizontal (nm)
No cooling No shims | 7,3 | 98
Cooling No shims | 18 | 150
Cooling Shims | 15 | 100
QF1FF/tabletop | Vertical (nm) | Horizontal (nm)
No cooling No shims | 20 | 150
No cooling Shims | 15 | 95
Cooling Shims | 16 | 120
More stable support gives better vibration behaviour
Support can benefit from upgrade study
Shims help but not significantly
Cooling has dramatic effect

## Slide 9: Another vibration source identified
This pipe has been placed so as to avoid touching girder
Unfortunately these cannot be changed easily in a quick fix
Sensor 2
After pipe repositioning
Sensor 1 still noisy, but vibration improvement
Step after step: vibration source identification

## Slide 10: ATF2 GM feedforward test
Goal
  Predict Ground Motion (GM) effect on beam trajectory with GM sensors
  Compare with BPM reading
Motivation
  Probably the first time GM sensors are compared to BPMs
  Demonstrate feasibility of a feedforward based on GM sensors
  Feedforward would allow trajectory correction based on GM sensors (get independant information between pulses)
  Possible big savings by relaxing mechanical quadrupole stabilisation specifications at CLIC
  Global scheme instead of local mechanical correction

## Slide 11: First results
GM effect small compared to orbit jitter: difficult experiment at ATF2
Incoming jitter can be measured by BPMs and removed from downstream BPM measurements
Low resolution BPMs at beginning
One can expect the GM effect can be detected by BPMs after jitter removal.
Typical “best” BPM () in vertical direction
BPM measurement with jitter removal vs BPM position predicted from GM sensor measurement: nice correlation!
Still need to evaluate if by removing strong vibration sources, this correlation remains
GM sensors powerful detecting vibration sources
Novel GM mitigation technique: promising!

## Slide 12: What was done by the French teams around ATF2
Introduction
Vibrations and GM feedforward
IP-BPM and chamber
Beam-halo evaluation : diamond sensor
Conclusion Outlook

## Slide 13: New IP-BPMs and chamber
A precise mover system (piezo movers PI and Cedrat) has been designed
 precise remote mechanical alignment of IP-BPMs (since in vacuum chamber)
 mechanical calibrations of IP-BPM scale factors with required precision (instead of moving the beam as before); their calibration, reproducibility and linearity below 10-4
In addition to the Beam Size monitor (Shintake Monitor), we also have Beam Position Monitors (BPM) around IP
A
B
C

## Slide 14
BPMs displacement system (inside chamber)
14
3 piezo-actuators/block for BPM vertical displacement ~300um
One piezo-actuators/block for BPM lateral displacement
~300um
IP
Measured versus predicted bunch position
res»26nm

## Slide 16: IPBPM alignments after recent re-installation
A
B
C
0.75mrad pitch
angle correction
Beam direction
A
B
C
200um vertical
misalignment
correction
We re-calculated the vertical misalignment
after 1.5mrad pitch angle correction with 900um shift up!
The average misalignment was 200um.
Beam direction
IP
IPA-YI’
IPB-YI’
IPC-YI’
200um
230um
167um
After the vertical misalignment correction about 200um.
Beam direction
IP
IPA-YI’
IPB-YI’
IPC-YI’
18.75um
13.75um
39um

## Slide 17: IP-BPM calibration
IP-BPM misalignment corrected so that beam passes through all 3 BPMs
IP-BPM calibration done
=> New IP-BPMs and improved IP-chamber operational!

## Slide 18: What was done by the French teams around ATF2
Introduction
Vibrations and GM feedforward
IP-BPM and chamber
Beam-halo evaluation : diamond sensor
Conclusion Outlook

## Slide 19
δp/p0=0.0008
Beam
Halo
Compton
DS scan
low energy (1.3GeV) prototype of the final focus system for ILC and CLIC
Accelerator Test Facility (ATF) @ KEK
Diamond Sensor
goal 1—achieving the 37 nm design vertical beam size at the IP;
goal 2—stabilizing the beam at that point at the nanometer level;
Goals of ATF2
Scan beam halo transverse distribution → investigate & control ATF2 beam halo
Probe Compton recoil electron→ investigate the higher order contributions to the Compton process
Interaction Point
Beam Size Monitor (IPBSM)
In Vacuum Diamond Sensor (DS)
Compton
Beam Halo -> major background for IPBSM !!!
S. LIU, P. BAMBADE et al., LAL-CNRS/IN2P3

## Slide 20
Beam Halo Scan
Preliminary
Total Beam intensity: 5.2*109
Voltage on DS: -400V
Total Beam intensity: 1.2*109
Voltage on DS: -40V
Beam Core Scan
Preliminary
@CIVIDEC
Installed at ATF2 in Nov. 2014
The first Diamond Sensor is installed horizontally at ATF2.
The main purpose is to measure the beam halo distribution.
Initial Waveform
Total Beam intensity: 1.2*109
Voltage on DS: -40V

## Slide 21
Beam Halo Scan
Preliminary
Total Beam intensity: 5.2*109
Voltage on DS: -400V
Total Beam intensity: 1.2*109
Voltage on DS: -40V
Beam Core Scan
Preliminary
@CIVIDEC
Installed at ATF2 in Nov. 2014
The first Diamond Sensor is installed horizontally at ATF2.
The main purpose is to measure the beam halo distribution.
Initial Waveform
Total Beam intensity: 1.2*109
Voltage on DS: -40V
Diamond Sensor operational and taking data in horizontal scan!

## Slide 22: What was done by the French teams around ATF2
Introduction
Vibrations and GM feedforward
IP-BPM and chamber
Beam-halo evaluation : diamond sensor
Conclusion Outlook

## Slide 23
French teams involved in ATF2 have signed E-JADE

## Slide 24: Conclusion Outlook
Contribute significantly to ATF2 Goal 2
  GM measurements and mitigation, aim at GM feedforward test , Halo measurements, Contribute to ATF2 beam size reduction and stabilisation with IP-BPMs
Contribute to ILC and CLIC
Successful in several Collaborations and great opportunity with E-JADE further harvest fruitful exchange with KEK experts
Publications and conferences
Training of students on a working accelerator (preparing future)
Getting precious experience to contribute to future machines and experiments!

## Slide 25: extras

## Slide 27: Diamond Detector Features
Property Diamond Silicon |  | 
Density (g m-3) Band gap (eV) Resistivity (Ω cm) Breakdown voltage (V cm -1) Electron mobility (cm2 V-1 s-1) Hole mobility (cm2 V-1 s-1) Saturation velocity (μm ns-1) Dielectric constant Neutron transmutation cross-section(mb) Energy per e-h pair (eV) Atomic number Av.min.ionizing signal per 100 μm (e) | 3.5 5.5 >1012 107 1700 2100 141 (e-) 96 (hole) 5.6 3.2 13 6 3600 | 2.32 1.1 105 103 1500 500 100 11.7 80 3.6 14 8000
In-vacuum single crystal CVD diamond sensor profile scanner -> for PHIL and ATF2 diagnostic (“plug compatible” design)
Test of fast remote readout (fast heliax coax cable + high BW scope) with particles at end of beam line, using existing single crystal 4.5x4.5mm CVD diamond pad sensor
Diamond detector test at PHIL
• Large band-gap⇒ low leakage current
• High breakdown field
• High mobility⇒ fast charge collection
• Large thermal conductivity
• High binding energy⇒ Radiation hardness
Fast pulse ⇒ several ns
ADVANTAGES