## Slide 1
2 Décembre 2014
F. Peauger, J. Plouin, B. Dalena, A. Mollard,
Chancé, L. Boudjaoui
CEA/IRFU/SACM
Nouveau concept de source de puissance 12 GHz pour CLIC
-
Third JCL (Journées Collisionneur Linéaire)
LPSC – Grenoble
-
Notes: Thanks Igor for invitation

## Slide 2: CLIC tunnel
Two beam acceleration concept where a high intensity drive beam is decelerated in order to produce RF power for the main beam acceleration
Single tunnel, no active elements inside
High frequency 12 GHz and high gradient 100 MV/m

## Slide 3: 12 Ghz two beam acceleration in CLIC
PETS with ON/OFF mechanism
high-power
low longitudinal and transverse impedance
necessary to react to breakdown and/or failure
Accelerating structure
high-gradient
length = 0.4 m
micron precision
transverse wake-field suppression
Waveguide network
high power
precise phase length
Drive Beam 100 A decelerated
Main Beam 1 A
accelerated
RF power 120 MW
We do not propose any alternative solutions to the PETS
x 32500 for 500 GeV
x 120750 for 3 TeV

## Slide 4: MASSIVE conditionning and TESTING CAPABILITIES of 12 GHz ACCELERATING STRUCTURES
TOSHIBA klystrons parameters
Frequency: 12 GHz
Peak power: 6 MW
Beam Voltage: 150 kV
Beam current: 90 A
Average power: 12.4 kW
Efficiency: 47.5%
I. Syratchev, G. McMonagle, N. Catalan Lasheras
The XBOX3 test stand at CERN will use four Medium Power X-band klystrons recombined and compressed to produce a 50 MW power level
We propose to design a new 12 GHz klystron with very high efficiency:
→ 70% for 12 MW output power
It will double the testing capability of an XBOX3 type test stand

## Slide 5
Propose and start long term technological R&D on high power RF systems, a key sub-system in an accelerator
Energy efficiency is highly important for future accelerators
  Reduction of power consumption and operation cost
  Limitation of the CO2 emission (social benefit)
  → mandatory for approval of new projects
Focus on RF source (klystron) efficiency only
wall plug
AC/DC power converter (modulators)
RF power source (klystrons, IOT,…)
useable RF
beam
loss
loss
Loss (40%)
loss
Φ & loss
E. Jensen
A strong motivation with a more general interest
Notes: On se propose de démarrer une activité de R&D technologique dans le domaine de la RF de puissance qui est un element clef dans un accelerateur et qui consomme enormement d’energie.
L’idée et donc de réduire la consommation electrique de ces systemes et en meme temps de limiter l’impact sur l’environnement.

## Slide 6: A strong motivation with a more general interest
This project is also an occasion to acquire knowledge and experience on RF sources “in-lab design” and why not “in-lab fabrication” in Europe
Some important projects (XFEL, ESS, CLIC-drive beam, FCC…) search for “green technologies” and so require ultra-high efficiency RF sources
A road map to reach the 90% efficiency horizon have been established at different frequencies

## Slide 7: What Limit the EFFICIENCY in a Klystron ?
Our proposal is to explore and invente new concepts for the higher perveance devices:
Simplify the modulator and the tube fabrication technology
But deal with very high space charge
The last 15 years was only focused on low perveance devices
ie. Multibeam klystrons (XFEL/ILC, CLIC Drive Beam)

## Slide 8: Reminder: What is a klystron?
It is a vacuum microwave electron tube amplifier where:
The input cavity prebunch slightly a DC beam provided by an electron gun
The intermediate cavities develop an RF voltage induced by the beam loading (image charges). These induced voltage intensify the bunching process.
The beam is strongly decelerated in the output cavity and a high RF power is created
The decelerated beam is collected in a collector
The beam is focused by an axial magnetic field (solenoid)
Image: courtesy of Thales Electron Devices
RF in
Axial electron velocity
RF out
S. Berger - Thales, XB2008 workshop, Cockcroft Institute, UK
Image charges

## Slide 9: A parallel with RFQs for proton linac
An RFQ cavity is used in proton linac injector to bunch, focus and accelerate a continuous beam from few tens of keV to few MeV.
It allows a beam transport in space charge regime (high intensity beams is possible) with very low beam losses.
bl
TE210 mode
longitudinal modulation on the electrodes creates a longitudinal component in the TE mode that bunch and accelerate the beam
In the IPHI RFQ (3 MeV, 6m, 352 MHz), around 350 cells are used to bunch the beam

## Slide 10: Phase space distribution in an RFQ
The bunching process in an RFQ is adiabatic (« gentle » buncher)
The RFQ preserve the beam quality, has a high capture (~90%) compare to a discrete bunching model (50%)
Phase (deg)
Energy dispersion dW (MeV)
At the RFQ exit:
Along the 6m RFQ:

## Slide 11: Increasing the number of cavities in a klystron
10 cavities
Efficiency 67.2 %
Length 197 mm
20 cavities Efficiency 78 %
Length 285 mm
→ Reduction of velocity spread of the beam

## Slide 12: Expected performances with 4 different designs
Name | Numbers of cavities | R/Q [Ohm] | TTF | Efficiency | Overall length [mm]
AK10-2 | 10 | 20 to 50 | 0.683 | 67.2 % | 197
AK14-1 | 14 | 20 | 0.683 | 68.5 % | 221
AK20-3 | 20 | 27.4 | 0.688 | 74 % | 285
AK20 | 20 | 12 | 0.72 | 78 % | 285
A new tube is born !
the Kl-adi(adiabatic)-stron =« KLADISTRON »
→ bunch the beam with a large number of small kicks instead of a small number of larger kicks
→ succession of quasi-equilibrium states
→ quasi-adiabatic bunching
70% efficiency

## Slide 13: Our sponsors
« In this sub-task, CEA will develop and search for innovative concepts of X band RF power sources and components. The objective is to propose affordable and reliable solutions for future testing capabilities for the CLIC accelerating structures. The task includes the design and the fabrication of prototype RF devices to demonstrate the feasibility of the new concepts proposed. »
WP12: Innovative RF Technologies
2013 - 2017
Achat du code de simulation PIC 2D / 3D (MAGIC)
Achat de sous ensembles (canon collecteur) d’un klystron existant à 4,9 GHz chez Thales
Contribution exceptionnelle de la France au CERN
AT4 – CLIC (2008 – 2014)
Thales electron Devices – Vélizy – RFMS
Fabricant de Tubes Electroniques Hyperfréquences
->Financement de 50% d’une bourse de thèse CTCI sur la période 2014-2017

## Slide 14: How to demonstrate the feasibility of the adiabatic concept
Buy an existing “cheap” THALES klystron:
TH2166 – 4,9 GHz – 25 kV - 4,5 A
Pout = 50 kW
6 cavities
Perveance = 1 µA/V^1,5
Efficiency = 45 %
Replace cavities by an adiabatic bunching structure
If necessary, modify solenoid (if longer bunching structure)
Kladistron 4,9 GHz
Goal efficiency =60%
Pout = 68 kW

## Slide 15: Beam / RF interaction simulation tools
MAGIC
PIC time domain
2D/3D
AJDISK
(SLAC)
1D
free
CST
PIC time domain
3D
WARP
(LBNL)
PIC time domain
2D/3D
Free, open source
Cluster
TRACEWIN
(CEA)
Tracking
2D/3D
Cluster
?
Frequency domain
2D
Preliminary design
Full verification of the performances and
oscillation study
Design consolidation
Emittance growth, matching, halo and error studies (new use for klystron!)
Remaining budget from the French exceptionnal contribution to CERN allowed us to buy one MAGIC licence
Collaboration with THALES will be extremely helpfull to benchmark with their homemade codes

## Slide 16: 12 GHz klystron Electron gun design and focusing solenoid
Figure 4: Beam created by the electron gun
Lyes BOUDJAOUI (Master 2 internship in 2014)
Simulation done using the CST-Particle Studio code
Benchmark to be perfromed with the THALES codes
Electron beam
170 keV – 100 A

## Slide 17: Beam/RF interaction simulatioN
Figure 4: Beam created by the electron gun
Franck PEAUGER, Barbara DALENA (Irfu/SACM)
Simulation done using the MAGIC2D code on a 14 cavities structure
Efficiency to be improved with output cavity optimisation
Electron beam:
170 kV – 100 A
Radius = 2.1 mm
Bz = 0.35 Tesla
Output RF power:
Pout = 8.8 MW for Pin = 15 W
Efficiency = 51.7 %
Gain = 57.7 dB
Oscillations damped after 150 ns

## Slide 18: Beam velocity simulation during bunching
Figure 4: Beam created by the electron gun
Simulation done using the WARP code
New Python class specially developed for klystrons (work in progress)
Barbara DALENA (Irfu/ SACM)

## Slide 19
The kladistron development planning
Preliminary design
2014
2015
2016
2017
Fabrication & Test
Detailed design and drawings
Choice of the number of cavities
Superconducting solenoid ?
PhD student (Antoine Mollard)
12 GHz
Kladistron
h = 70%
Prf = 12 MW
4.9 GHz
Kladistron
h = 60%
Prf = 68 kW
Design
Tests
Fabrication
Superconducting RF structure ?
If additionnal ressources available

## Slide 20: Conclusion
New concept of high efficiency klystrons proposed
Based of beam dynamic knowledge already present in SACM (RFQ)
Development plan established in collaboration with an world leading industrial
Additional ressources needed to complete the fabrication of the 12 GHz kladistron

## Slide 21: Extra slides

## Slide 22
CLIC 3 TeV layout
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 23
31 km, ~100 m deep
14 km, ~100 m deep
CLIC site at CERN

## Slide 24
CLIC main parameters
Center-of-mass energy | ILC 500 GeV | CLIC 500 G Nominal | CLIC 3 TeV Nominal | 
Total (Peak 1%) luminosity | 1.8(1.5)·1034 | 2.3(1.4)·1034 | 5.9(2.0)·1034 | 
Repetition rate (Hz) | 5 | 50 | 50 | 
Loaded accel. gradient MV/m | 31.5 | 80 | 100 | 
Main linac RF frequency GHz | 1.3 (SC) | 12 | 12 | 
Bunch charge109 | 20 | 6.8 | 3.72 | 
Bunch separation ns | 554 | 0.5 | 0.5 | 
Beam pulse duration (ns) | 1312 | 177 | 156 | 
Beam power/linac (MWatts) | 10.2 | 4.9 | 14 | 
Hor./vert. norm. emitt (10-6/10-9) | 10/35 | 2.4 / 25 | 0.66/20 | 
Hor/Vert FF focusing (mm) | 11/0.4 | 8/0.1 | 4 / 0.07 | 
Hor./vert. IP beam size (nm) | 474/ | 202/ 2.3 | 40 / 1.0 | 
BDS length (km) | 2.23 (1 TeV) | 1.87 | 2.75 | 
Total site length (km) | 31 | 13.0 | 48.3 | 
Wall plug to beam transfer eff. | 9.4% | 7.5% | 6.8% | 
Total power consumption MW | 163 | 270 | 589 |