## Slide 1: XFEL couplers production status
Third JLC (Journées collisionneur linéaire )
Hayg GULER

## Slide 2: Outline
General introduction
Production and monitoring at companies
Coupler preparation and RF conditioning at LAL
Status of the XFEL couplers production
Projections for the ILC

## Slide 3
1.3 Km e- cold linac reaching up to 17GeV
Introduction

## Slide 4
Linac composed of 100 Cryomodules, equipped with 8 couplers each  800 Couplers needed
Introduction

## Slide 5
Introduction
Notes: Vision générale  Vue de dessous du cryomodule : La partie froide du coupleur est fixée à la cavité supra.
Parler de la supra vs la zone a temperatue ambiante.

## Slide 6
Introduction
Notes: Un coupleur XFEL doit remplire 3 fonctions :
Transmission de la RF entre une source vers les cavités supra
Séparation thermique : entre milieur a temperature cryogenique et milieur a temperature ambiante
Transition vide ultra vs vide (double separation via les ceramiques pour eviter que le vide froids se deteriorent)
assurer un couplage électrique (variable) avec les cavités via son antenne introduite au niveau du tube de faisceau à l’entrée du résonateur
Conducteur interne polarisable ?
Partie chaude
Partie froide
Une transition guide d’onde

## Slide 7: Production monitoring at companies
Brazing, Copper plating
TiN Coating, Welding
RF Conditioning
Cryogenic modules
Installation on tunnel
Notes:   Thales
    Assemblement des pairs (Brasage)
    Cuivrage des parties des coupleurs
    Implications dans la station de conditionnement
  RI
    Pose colleret cuivre aux ceramiques
    TIN Coating sur les ceramiques
    Soudure par faisceau d’e- : associe antenne partie haute de la ceramique + partie basse du coupleur froid
    Lavage des coupleurs : bain ultrasonique + détergent (Ticopure)
    Comptage des particules (propreté des coupleurs)
    RGA + Leak test
    Test de déplacement de l’antenne

## Slide 8
At Thales site:
1st step: parts assemblies by brazing:
2nd step: RF Surfaces copper plating of the assembled parts:
Production monitoring at companies
Thales
Notes: Brasage céramique/cuivre

## Slide 9
Weekly inspection meetings organized at Thales-Thonon to control parts copper plating quality
Cold part
Warm part
Production monitoring at companies
Thales : inspections

## Slide 10
Production monitoring at companies
List of possible defects to reject coupler part
x 40
x 30
x 22
… with derogation
… After particle removal
… with derogation
Inspection criteria document

## Slide 11
At RI site:
Production monitoring at companies
RI (Köln)
Notes: TIN Coating pour diminuer les coeficients d’emission secondaire, pour diminuer la formation de multipactors.

## Slide 12
Shipment to LAL
Production monitoring at companies
RILAL

## Slide 13
ISO 5 clean room
ISO 7 clean room
Control room
Changing room
Airlock staff
Couplers preparation and RF conditioning at LAL

## Slide 14
Couplers preparation and RF conditioning at LAL
List of actions to prepare RF conditioning
75h baking cycle at 130°C
Leak test after reception
Antenna tuning
RGA spectrum recording
WGBs assembly
Capacitors assembly
Actuators assembly
Notes: Etat des temoins de chocs + absence de degradation des boites de transport
Presence des (sous) ensembles, integrites sacs de transport
Aspect general des coupleurs, conformite des etats de surface
Proprete des coupleurs
Gravage des parties et sous parties
Tests de fuite  Toute une procedure bien detaillee

## Slide 15
Couplers preparation and RF conditioning at LAL
Coupler on RF test bench : list of diagnostics
Notes: Vision schematique des coupleurs sur banc de conditionnement.
Sont visibles la liste des diagnostiques : pickups, vides, niveaux de puissance incident et reflechie.
Voir quels detecteurs sont utilises pour mesurer les puissances (diode ?)

## Slide 16
Couplers preparation and RF conditioning at LAL
RF station at LAL

## Slide 17
Couplers preparation and RF conditioning at LAL
Split power into 4 conditioning lines
Ligne D
Ligne C
Ligne B
Ligne A
PicD
PicC
PicA
PicB
PrcD
PrcC
PrcB
PrcA
PchC
PchB
PchA
V1A
V3A
V2A
V1B
V3B
V2B
V1C
V3C
V2C
V1D
V3D
V2D
PchD
Arcil1A
Arcil2A
Arcil1B
Arcil2B
Arcil1C
Arcil2C
Arcil2D
Arcil1D
Notes: Discussion sur les detecteurs d’arc
Discussion sur l’utilite d’itiliser les SF6 comme gaz dans les guides d’onde

## Slide 18
Couplers preparation and RF conditioning at LAL
LAL cleaned room with 4 coupler lines

## Slide 19
Couplers preparation and RF conditioning at LAL
RF conditioning sequences scheme
Algorithm based on pressure level :
While (pressure < SV1=6.10-7 mBar)  Power increases by 0.1 dB

## Slide 20
Couplers preparation and RF conditioning at LAL
RF conditioning DATA : Power sequences

## Slide 21: Conditioning effect on current levels Pickups vs Power (20µs pulse)

## Slide 22: Conditioning effect on current levels Pickups vs Power (50µs pulse)

## Slide 23: Conditioning effect on current levels Pickups vs Power (100µs pulse)

## Slide 24: Conditioning effect on current levels Pickups vs Power (200µs pulse)

## Slide 25: Conditioning effect on current levels Pickups vs Power (400µs pulse)

## Slide 26: Conditioning efficiency
High vacuum and current levels at low power disappear after the first conditioning steps.
  This region corresponds to unstable multipactor area and degasing power which appears at P<150kW.
Vacuum and current levels around the stable multipactor area (300 to 800 kW) stay high until the last steps.
At the end of conditioning we expect less than 10-7 mBar pressure and quite low (<1V) pickups levels

## Slide 27
Couplers preparation and RF conditioning at LAL
RF conditioning software

## Slide 28: Conditioning duration : needs and reality
Needs: 8 couplers/Week
Baking : 3 ½ days
Remote control
RF conditioning : up to >100h
Increase baking temperature
RF station stabilized
RF conditioning:
< 40h
Possibility : 12 couplers/week

## Slide 29
Couplers preparation and RF conditioning at LAL
Notes: Apres conditionnement

## Slide 30
Couplers preparation and RF conditioning at LAL

## Slide 31
Couplers preparation and RF conditioning at LAL

## Slide 32
Status of the XFEL couplers production
The nominal rate of 8 coupler/week delivered from LAL to IRFU was reached beginning March 2014, however still some instability in the deliveries from companies.
Back to nominal rate since > 1 month
First couplers were tested successfully in cryomodules (11 modules already tested at DESY).

## Slide 33: Coupler delivery schedule :
240 couplers to date
Status and schedule of couplers deliveries to IRFU-CEA
Loading…
8 CP/W
264 couplers
End 2014
656 couplers
End 2015
June 2013
800 couplers
May 2016

## Slide 34: Coupler delivery schedule :
Loading…
8 CP/W
264 Cps
End 2014
656 Cps
End 2015
June 2013
800 Cps
May 2016
336 Cps
Loading…
10 CP/W
240 Cps
To date
End March 2015:
CPI production- 8Cps/2W
March 2016
Loading…
12 CP/W
End January 2016
8 CP/W

## Slide 35
 | XFEL | ILC 250 | ILC 500
Energy | 17 GeV | 250 GeV | 500 GeV
Modules | 100 | 992 | 1924
Couplers | 800 | 7936 | 15873
XFEL is considered as a good training and a major asset for LAL to be a key player in ILC construction.
Scenario for 10x more couplers needs :
  production should be shared between many (Industrial, LAB) couples
  Common acceptation criteria should be used
    With regular checks and/or cross checks
  Still room for improvement
    Industrials for their process
    Baking/conditioning processes but no miracles
From XFEL to ILC…

## Slide 37
Thanks for your attention.