## Slide 1: Design for Fe-55 Source
D.G. Kelly, E.C. Corcoran, P. Samuleev and T. Mumby
NEWS-G Collaboration Meeting
Grenoble
11-13 June 2019

## Slide 2: Fe-55 Source: Activity
  Fe-55: half-life 2.70 years, decay 5.95 keV
  Activity
    1 mBq effective activity
    Accuracy  50%
  Physical
    Sealed
    Isotropic, anisotropic, both

## Slide 3: Fe-55 Source: Physical
  Location
    Rod
      Removable – accessed from bottom
  Size
    Rod diameter: 6 mm…consistently?
      Concentric source diameter: 10 mm

## Slide 4: Fe-55 Source: Physical
  Materials
    Aluminium
      High purity (5N in 10 mm and 12 mm Ø)
    Others
      Commercial Al alloy
      Copper
      Steel?
      Carbon-based: epoxy

## Slide 5: Design
  Sleeve
    Grubb screw(s)
    Annular well(s)/channel for source
    Add source, seal with epoxy
Grubb screw(s)
1 mm depth
channel or
1 mm holes

## Slide 6: Fe-55 Source: Commercial
  Nominal 3.7 kBq Fe-55 solution in 5 mL
    Readily available: $1,200
    0.1 M FeCl3 solution
  Use
    Dilute in high purity aq. HNO3
    Add Fe(III) carrier
    Electroplate

## Slide 7: Fe-55 Source: Commercial
  Nominal 3.7 kBq Fe-55 solution in 5 mL
    Why not simply…
      Dilute (1 in 100) x 3
      Drop 1 L in place and allow to dry
      Seal with epoxy
    Good question!

## Slide 8: Fe-55 Source: NAA
  Natural iron not ideal source
    Fe-59: 45.1 day half-life
    Fe-59: 1099 and 1292 keV gammas, plus several others down to 143 keV

## Slide 9: Fe-55 Source: NAA
  Isotopically enriched Fe-55
    > 99.85 enriched Fe2O3 (powder)
    > 99.70 enriched metal (granules)
      Purchased: 2 x 100 mg, $2,000
    Irradiation
      1 mg metal, 5x1011cm-2s-1, 9 sec, 1 Bq activity
      ↓ mass Fe-54, ↓ flux, Cd shield, attenuate in place

## Slide 10: Detection
  5.9 keV too low for HPGe
    Not quantitative

## Slide 11: Fe-55 Source: Attenuation
  MCNP
    Simple model to consider effects of…
      Sleeve
      Epoxy
      Additional materials

## Slide 12: Conclusion
  Access to Fe-55 simple: purchase or activate
  Low activity
    Easier with aqueous Fe-55
  Sealing
    Easier with activated metal or oxide