## Slide 1
Henry Klest
Argonne National Laboratory
CALORIMETRY FOR THE ePIC EXPERIMENT

## Slide 2
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:

## Slide 3
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:
  Particle ID: Chandra’s talk

## Slide 4
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:
  Particle ID: Chandra’s talk
  Tracking & Vertexing: Gian Michele’s talk

## Slide 5
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:
  Particle ID: Chandra’s talk
  Tracking & Vertexing: Gian Michele’s talk
  Far-forward detectors: Michael’s talk

## Slide 6
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:
  Particle ID: Chandra’s talk
  Tracking & Vertexing: Gian Michele’s talk
  Far-forward detectors: Michael’s talk
  Calorimetry: this talk

## Slide 7
Epic at the EIC
  EIC is a high luminosity machine, enabling precise measurements (Shujie’s talk)
    Much of the EIC physics lives in percent-level effects
    Requires precision in:
  Particle ID: Chandra’s talk
  Tracking & Vertexing: Gian Michele’s talk
  Far-forward detectors: Michael’s talk
  Calorimetry: this talk
  Cross-check! – Pawel’s talk

## Slide 8
Calorimetry at the Eic
  Calorimetry at the EIC has some unique challenges:
    Wide variety in CM energy, 5 GeV e- x 41 GeV p/A to 18 GeV e- x 275 GeV p
  EIC physics lives at all scales!
    Large dynamic range required, hundreds of GeV to tens of MeV
    Most challenging constraint is not always simply measuring energy
  Electron identification
    Very stringent requirements on e/h separation to identify DIS events from the much larger photoproduction background
    1-in-10000 rejection of pions in the few GeV range!
  Streaming readout
  Integration with PID & tracking detectors

## Slide 9
Calorimetry at the Eic
p/A
e-

## Slide 10
Calorimetry at the Eic
“Forward”
“Backward”
Hadronic final state
Scattered electron
Hadron beam remnant

## Slide 11
Backward calorimeters
Hadronic final state
Scattered electron
Physics:
gluon saturation, nuclear terra incognita
Challenge:
Measure the electron with high precision at small scattering angles
Separate the scattered electron from the nearby hadrons
Hadron beam remnant
Low Q2, low x

## Slide 12
Backward calorimeters
Hadronic final state
Scattered electron
Resolution requirements: EMCal:
HCal:
Hadron beam remnant
Low Q2, low x

## Slide 13
Backward electromagnetic calorimeter
  Largest cross section for small electron scattering angles
    Captures vast majority of scattered electrons
    Often better resolution than tracker in this region
  Required energy resolution of
    For most electrons, dominated by constant term
    Need precise mechanical construction & calibration techniques
  1 in 104 pion suppression
  Detection of photons above 50 MeV
  Radiation hardness

## Slide 14
Backward electromagnetic calorimeter
  Only realistic option to meet all of these requirements is PbWO4
    High density (small Molière radius), high scintillation light yield, fast scintillation, rad hard
    Readout via HPK S14160-3010PS SiPMs

## Slide 15
Backward electromagnetic calorimeter
  PbWO4 light yield is a strong function of temperature, ~2% per C°
    Big integration challenge, pfRICH electronics sits nearby
    Needs temperature stability & monitoring to reach resolution goals
  Non-trivial interplay between achieving temperature stability and reducing dead material between the crystals
    Crystals held by two 0.5 mm thick carbon fiber frames
    One in front 2 cm of a block, one in back 2 cm
    Air gap in-between

## Slide 16
Backward hadronic calorimeter
  Experience from H1 & ZEUS, backward HCal useful for improving e/h separation at low-x
    Electron & hadrons go in the same direction, substantial overlap in the EMCal
  Low-x hadronic final state important for studying gluon saturation, typically backward-going
  Hadron energies are low, serves in part as a tail-catcher for the EMCal
    Energy resolution requirements not stringent
    Position resolution should be good enough to match Hcal clusters to energy deposits in Emcal
  Exact design still in progress, some combination of steel + large scintillator tiles & SiPM readout
    Similar to BELLE KLM

## Slide 17
Barrel calorimeters
High Q2, Mid x
17
Hadronic final state
Scattered electron
Example Physics: DVCS, DVMP
Challenges:
Identify components of hadronic final state, e.g. separate from ɣ
Identify low energy e- from high y DIS
Contain 30+ GeV energy e- from high Q2
Measure low energy ɣ

## Slide 18
Barrel calorimeters
Hadronic final state
Scattered electron
High Q2, Mid x
Resolution requirements: EMCal:
HCal:

## Slide 19
Barrel electromagnetic calorimeter
  Hybrid sampling Pb/SciFi + Silicon pixel sensor
  4.4 m long scintillating fibers, SiPM readout on both ends
    Longitudinally segmented
    Similar to KLOE & GlueX
    “Time-Projection” calorimeter -
    HGCROC for front-end electronics
  Interleaved with layers of AstroPix MAPS silicon pixel sensors
    Very low power consumption (few mW/cm2)
    500 μm “cube” pixels
    Good resolution (~7%) on energy deposited in pixel

## Slide 20
Barrel electromagnetic calorimeter
SiPM Readout Scheme
Light guides to 1.2x1.2 cm SiPMs
AstroPix Tiling Options
~10 cm

## Slide 21
Interleaving of AstroPix sensors allow for excellent position resolution
  Angular resolution on the order of 0.1 degree
  Separate from ɣ beyond 30 GeV
  Can do vertexing on photons!
separation factor
Very effective separation of electrons from hadrons based on shower shape discrimination
  Still quite effective at ~1 GeV & below

## Slide 22
Barrel Hadronic calorimeter
  Modest requirements on energy resolution
    ~ 100%/
    Hadrons in barrel typically low energy (<5 GeV), better measured by tracking
    Tag jets with large neutral hadron component
  Measure muons from e.g.
  Reuse from sPHENIX
22

## Slide 23
Barrel Hadronic calorimeter
  Steel/Scintillator design
    Steel plates tiled at an angle to prevent channeling
    Straight tracks have a sizable path length through scintillator, good for MIP detection
    Readout via HPK S12572 series SiPMs
  Refurbish for EIC
    Expect minor radiation damage from sPHENIX, can replace SiPMs with HPK S14 series
    Upgrade electronics to HGCROC
    Increase segmentation by reading out each tile individually
23

## Slide 24
Forward calorimeters
Hadronic final state
Scattered electron
Example Physics: TMDs, Jets, SIDIS
Challenges:
Contain the highly energetic hadronic final state
Separate clusters in a dense hadronic environment
Highest radiation load near hadron beam
High Q2, High x

## Slide 25
Forward calorimeters
Hadronic final state
Scattered electron
High Q2, High x
Resolution requirements: EMCal:
HCal:

## Slide 26
Forward electromagnetic calorimeter
  Tungsten + SciFi SPACAL design
    Developed through EIC R&D and applied successfully in sPHENIX EMCal
    Tungsten powder mixed with epoxy
  Position resolution vital to separate from ɣ at high energy
    Dense absorber (~10 g/cm3)
    Readout with many SiPMs to create a small tower size
  Uniformity of construction important to reduce constant term
    Dominates at high energy
    Powder + epoxy enables fine control over spatial distribution of scintillator

## Slide 27
Forward electromagnetic calorimeter
  5 cm x 5 cm x 17 cm blocks of absorber + fibers
    Four independent towers per block
  Each 2.5 x 2.5 cm tower is readout by four 6x6mm HPK S14 series SiPMs
  Expected energy resolution ~

## Slide 28
Forward hadronic calorimeter
  Steel + Scintillator SiPM-on-tile
    Pioneered by CALICE analog HCal
    Ideal for particle-flow measurements!
  Highly segmented longitudinally, 65 layers per tower
    565,760 SiPMs
    65 layers ganged into 7 readout channels
  Stackable for “easy” construction
    Steel as absorber significantly simplifies design, improves material uniformity
    Achieves ~6.5
  Expected resolution ~
    Exceeds requirements defined by Yellow Report!

## Slide 29
Forward hadronic calorimeter
  SiPMs mounted to thin flex PCBs
    Signals routed along PCB to periphery
  Signals brought to HGCROC at back by a thin flex PCB that runs longitudinally alongside the tower

## Slide 30
Forward insert calorimeter
  Insert to extend central detector acceptance as much as possible in the forward direction
    Crucial for containment of hadronic final state for inclusive kinematic reconstruction and rapidity gap diffractive measurements
    3.2 < η < 4
    Needs to accommodate complex beam pipe geometry
  Small hexagonal scintillator tiles for better spatial uniformity & increased light yield
  High radiation load
    SiPMs will be serviceable
    ~1012 neq/cm2/year

## Slide 31
Performance projections
  High radiation load
    SiPMs will be serviceable
    ~1011 neq/cm2/year

## Slide 32: Conclusion
Calorimetry is a vital component of the EIC detector package
ePIC employs unique calorimetry designs to meet the varied demands of the different detector regions
  Designed to meet the multifarious challenges & physics of the EIC!
The ePIC calorimeter designs meet or exceed their performance requirements!
Thanks to everyone who provided the information for this talk!
EIC is scheduled to begin running in 2032
  CD3 & Construction to begin in earnest in 2025
ePIC TDR coming soon, stay tuned!
Thank you!

## Slide 33: Backup

## Slide 34
2x2x20 cm3 PWO crystals
0.5-mm-thick C-fiber between crystals along 2 cm in the front & back; 0.5 mm of air elsewhere
diameter:
EMCAL
DIRC
Beam pipe
Interaction point
174 cm
FRONT
BACK

## Slide 40: Backup