## Slide 1: Development and characterisation of detectors for beam monitoring in radiotherapy
Jayde Livingstone
Equipe Physique Nucléaire et Applications Médicales, LPSC, Grenoble
IUT1 Mesures Physiques

## Slide 2: Development and characterisation of detectors for beam monitoring in radiotherapy
Jayde Livingstone
Equipe Physique Nucléaire et Applications Médicales, LPSC, Grenoble
IUT1 Mesures Physiques
2014
2015
2016
2019
2017
2018
2020
2021
2022
2023
2024
Beamline scientist
(synchrotron radiotherapy)
IMBL, Australian synchrotron
Postdoc: online range monitoring proton therapy
LPSC – IP2I
Source modelling for virtual imaging
NOVITOM
AI-based classification & segmentation histology
UGA - MOREHISTO
Nanoscale phase contrast imaging
ESRF
Diamond-based beam monitors
LPSC

## Slide 3: Development and characterisation of detectors for beam monitoring in radiotherapy
Jayde Livingstone
Equipe Physique Nucléaire et Applications Médicales, LPSC, Grenoble
IUT1 Mesures Physiques
2014
2015
2016
2019
2017
2018
2020
2021
2022
2023
2024
Beamline scientist
(synchrotron radiotherapy)
IMBL, Australian synchrotron
Postdoc: online range monitoring proton therapy
LPSC – IP2I
Source modelling for virtual imaging
NOVITOM
AI-based classification & segmentation histology
UGA - MOREHISTO
Nanoscale phase contrast imaging
ESRF
Diamond-based beam monitors
LPSC

## Slide 4: What is radiotherapy?
Use of radiation radiation (e.g. x-rays, electrons, protons, etc.) to treat a disease
About half of all cancer patients will receive some form of radiotherapy during their treatment
The goal of radiotherapy is of course to kill cancer cells…
But not at the expense of healthy cells!
The dose to healthy tissue must remain below a threshold for normal tissue complications
Chart: Dose (Gy)
Tumour control
Normal tissue complication
Therapeutic ratio

## Slide 5: Increasing the therapeutic window
Arjomandy, J. Proton Therapy, 1(1), 2015
Thariat J., et al., Lancet, 22(12), 2021

## Slide 6: Innovative techniques: spatial fractionation
Curtis, H. J., Radiat. Res., Suppl. 7., 1967
Dose volume effect
Mohiuddin et al., Cureus, 7(12), e417
GRID radiotherapy (~cm beams)
“Innovative” – first proposed in 1909
Widely used from the 1930s to 1970s
Became obsolete with MV radiotherapy
Limitations

## Slide 7: Pushing Spatial fractionation to extremes
Microbeams (~10s of µm)
Minibeams (~several mm)
http://mswebs.naist.jp
www.esrf.eu
Mazal A, et al., Br J Radiol 2020; 93: 20190807
X-rays only: currently confined to synchrotron sources due to spectrum (kV) and high dose rates (102 – 103 Gy/s) required
X-rays and charged particles (eg. protons) Technically less challenging, lower risk

## Slide 8: INNOVATIVE TECHNIQUES: FLASH
8
Lung fibrosis in mice:
Severe
Moderate
Mild
Minimal
Favaudon et al., Sci. Transl. Med., 6, 245ra93, 2014
Healthy tissue sparing effect at ultra-high dose rates (≥40 Gy/s)
First observed by Favaudon et al. in 2014 using electrons
Extended to x-rays and protons
Could be combined with spatial fractionation

## Slide 9: Challenges for treatment planning, delivery and beam monitoring
A) Range uncertainties in proton therapy
B) Beam monitoring in high dose rate environments
C) Micrometric beamlets and high dose gradients
e-h recombination
Radiation induced damage
Knopf et al., Phys. Med. Biol., 58, 2013
Requirements: tissue equivalence, rapidity, radiation resistance, high spatial resolution, dose rate independence, wide dynamic range
Monitoring the transmitted proton beam is not an option
(there is very little to no transmission!)
Secondary radiation detection

## Slide 10: Online range monitoring for proton therapy (postdoc LPSC 2018-2019: CLARYS-UFT)
Krimmer et al., NIM A, 878, 2018

## Slide 11: Online range monitoring for proton therapy (postdoc LPSC 2018-2019: CLARYS-UFT)
Livingstone et al., Phys. Med. Biol., 66, 2021
Reconstruction: Compton camera

## Slide 12: Instrumentation for microbeam radiation therapy
Livingstone, et al., J. Synchrotron Rad., 24., 2017.

## Slide 13: Characterisation of a diamond detector for microbeam radiation therapy
microDiamond (PTW Freiburg, Germany)
2 mm
1 µm
Active volume:

## Slide 14: Characterisation of a diamond detector for microbeam radiation therapy
Livingstone et al., Med. Phys., 43, 2016

## Slide 15: IDSYNCHRO: Diamond-based Microstrip detector for MRT monitoring
PhD: Candice Milewski (1st year)

## Slide 16: DIAMMONI: Diamond-based beam monitor for proton flash therapy (arronax)
Diamond:
Rapid
Low leakage current
High SNR
Radiation resistant
Tissue equivalent
PhD: Robin Molle (3rd year)
sCVD vs pCVD
Dose rate linearity
Lifetime (radiation damage)
Electrical/charge transport properties
  Measured and simulated (ECORCE)
GATE simulations
Internship: Nicolas André (commencing 5th of February)