## Slide 1: The LHC ultimate beam(*): Stretching the LHC RF system to its limits
RFTech WS, PSI , 2-3 Dec 2010
J. Tückmantel, CERN-BE-RF
(*) 1.71011 p/bunch, Tb=25ns

## Slide 2
Contents:
• Task of the (LHC) RF system
• Beam-Loading
• Reactive Beam-Loading (Compensation) (RBLC)
• Gaps in the (LHC) Beam
• Averaged RBLC: ‘Let the Bunches Slide’
• The ‘case LHC’ compared to electron-machines
• Setting bunches and defining the Voltage set-function
• Get some numbers (... kW, … kHz, )
• Summary
{ Appendix A, B: Cavity-transmitter-beam lumped circuit model }
{ Appendix C: Bunch Form Factor }

## Slide 3
Task of the LHC RF system
• Accelerate the beam (CERN is accelerator center ...)
beam must be made of particle lumps: bunches
(shorter than to λRF)
• In coast :Conserve bunch structure:
All particles have slightly different energy/revolution time
-> Without RF voltage (slope) bunches would dissolve
and fill up the whole ring (‘uniform saussage’)

## Slide 4
Beam Loading (= Energy conservation !)
An accelerated charge q takes energy:
taken from the stored energy of the cavity (‘instant’, ‘forget’ transmitter)
Cavity (shape) constant (R/Q) (circuit Ω convention)
Before q: cavity voltage V After q: V’=: V+ΔV
q takes energy ΔUq= q (V + μ ΔV)
including yet unknown fraction μ of its own induced ΔV:
Cavity energy changes by the same energy
Superposition V, ΔV: must be valid for any V
also valid for complex V and ΔV: “ΔV and V any phase”

## Slide 5
• Any q induces a (decelerating) voltage
independent of any already present V, including V=0
(superposition !)
• Any charge q feels half of its own induced voltage
Fundamental Beam Loading Theorem
(Perry Wilson, 1974)
Example LHC ultimate bunches: 1.7E11 p = 27 nC;
(R/Q)=45 Ω, ω = 2π 400 MHz
 ΔV = –3.1 kV (while V = 1 … 2 MV / cavity)

## Slide 6
In LHC bunches ride 90º out of phase wrsp. to RF voltage:
No energy transfer in coast
(Acceleration on long LHC ramp very weak: neglect here)
 Induced ΔV 90º out of phase wrsp. to V (… ‘reactive’ …)
Reactive Beam-Loading (Compensation)

## Slide 7
Reactive beam loading will ‘kill’ beam if no counter-action
Bully method: (large amount) of RF power pushes
vector back to nominal
Clever method: Detune cavity (by the right amount) !
During inter-bunch time Tb=n*TRF voltage vector turns
not only n times but a bit more/less to nominal again!
Named: Reactive beam loading compensation (RBLC)
Example LHC ultimate: Tb=25ns; ΔV = 3.1 kV; V = 2 MV  Δϕ=ΔV/V=1.55 10-3 rad
Δω Tb = -Δϕ  |Δf|=9.9 kHz (no practical problem)
{Δf< frev large V, small (R/Q) : main reason for choice of LHC superconducting cavities}

## Slide 8
Problem: Clever method relies on regular bunch arrival,
No longer(*) gaps in bunch sequence allowed !!
…. but LHC has many long gaps:
1 beam dump (3µs), 11x SPS/LHC kicker (24+ PS/SPS kicker)
(mechanical) tuner much too slow to ‘jump’: one Δf chosen ….
Δf chosen for bunches: OK if bunches ‘tough’ in gap
Δf=0 chosen: OK in gap ‘tough’ if bunches
‘Clever Bully’ (Daniel Boussard): use half-detuning
(*) Long gap: lasts a sizable fraction of the natural time constant of the RF system
with RF vector feedback (i.e. very few missing bunches are averaged out)
Gaps in the (LHC) Beam

## Slide 9
Half-detuning Δf recovers half of the bunch’s ‘perturbation’
• with bunches (‘on train’): RF power pushes the remaining half
• without bunches (gap): RF power pushes back what cavity did
Needs for both cases only (½)2 = ¼ of the (additional)
RF (peak!) power … compared to either full or no detuning

## Slide 10
Till now: only regular bunch spacing allowed
If each next bunch would arrive at a slightly shifted position
when the total RF voltage – including all accumulated ΔV of pervious bunches – is zero anyway ?!?
 no RF power would be needed to ‘push’ back/forward
But: Shifts accumulate and periodicity over one turn not
fulfilled anymore !
Solution: Detune cavity such that it compensates the accumulated phase-shift averaged over one turn !!
Example LHC: 2806 bunches, 3564 possible positions
(756 ‘holes’): Σ(Δϕ)=2806*1.5510-3 rad = 4.35 rad
Trev=3564*25 ns=89 µs  Δω=-4.35/89 µs  |Δf|=7.7 kHz
Fortunately in LHC not one big but many gaps: ‘dilutes’
Averaged RBLC: ‘Let the Bunches Slide’

## Slide 11
The cavity quadrature voltage (‘in phase with beam’)
Beam dump gap
SPS/LHC kicker gap(s)
PS/SPS kicker gap(s)
Periodic over 1 turn
J.T.:”The LHC Beam with Suppressed RF Transients”, CERN-AB-Note-2004-022
on http://cdsweb.cern.ch/

## Slide 12
The longitudinal bunch position (1 cm = 33 ps)
(4σ-bunch length 30 cm >> max. displacement)

## Slide 13
Have assumed that ‘bunches sit on desired position’
How do we get them there ?
In e-machines synchrotron radiation damping (some … ms)
allows ‘nearly everything’
– Inject ‘bunchlets’ into already occupied buckets
(as in LEP / PEP || ‘topping up’):
‘adiabatically’ accumulating beam, bunches settle
– Shake the beam without permanent emittance blow-up;
e.g. displacing RF zero crossing: bunches follow
and contract on new bunch center
– ……
The ‘case LHC’ compared to elec.-machines

## Slide 14
In LHC there is ‘no’ such damping (7 keV/turn at 7 TeV/c):
‘protons never forget what you did to them’
– Have to inject full bunches (no bunchlets) in one ‘bang’
(‘SPS batch’ of ≈ 250 bunches injected into LHC)
– Bunches are regularly spaced from injector (SPS)
– Even if bunches would be pre-displaced, sudden injection
would disrupt ‘equilibrium of displaced bunches’ in LHC
During the injection we need enough RF power to
capture and keep regularly spaced bunch trains (batches)
– Possible up to ultimate (*) since injection done at only
1 MV/cavity (even lower V: capture losses)
– Nominal beam can (just(*)) be accelerated and coasted
with 2 MV/cavity and regular spacing
(*) The slight averaging over gaps helps to have enough power for transients

## Slide 15
Setting bunches and defining V set-function
The problem:
Initially regular bunches and a constant V-set-value V0
 Want to have bunches at a position they would take if
V would only be governed by beam-loading(*)
 The voltage set-value has to become a set-function
– periodic & synchronous with the beam turn
– programming the voltage the beam would create anyway
(else large (FB gain !!) transients to ‘enforce the error’)
Calculating impossible: perfect knowledge of ALL parameter(+)
? ? ?
(*) Only the natural field decay by Qext, Q0 is restored by the transmitter
(+) Cavity Δω, Qext, all bunch charges (!), cable delays, ….

## Slide 16
Use LHC as ‘analogue computer’: parameters perfect
(the world most expensive one !)
The ‘classical’ RF Feedback Loop in an Accelerator
Takes and gives power !!
Reacts on
cavity voltage !!
J.T.: “Adaptive RF Transient Reduction for High Intensity Beams with Gaps”, EPAC 06
http://cern.ch/AccelConf/e06/PAPERS/MOPLS006.PDF
-> insertion of special device ‘smoother’ at α (β equivalent)

## Slide 17
Digital ‘smoother’
Passive cyclic
set-funct. buffer:
Under preparation for swap
Active cyclic
set-funct. buffer:
Play back sync.
with beam turn
Cyclic buffer:
Data recording 1 turn =
3564 positions / data
(+ possib. averaging)
(digital) variable local gain (e.g. range factor 1 -> 0.5)

## Slide 18
1) Adiabatically lower local gain
(e.g. to 90%)
• Smoothes ‘edges’ of transients
• Feedback still active
(90% total gain ..
but beam still stable)
2) Calculate Sp such(+) that with g=1 it would create the same signal ‘d’ as now
3) Simult. (*) • swap Sp to active one • local gain back to 1
Operation is transparent elsewhere, also for beam (!!)
(*) best start of b. dump gap (time to recover µ-transients if execution not perfect)
(+) … and Sp = Sp – <Sp> (keep zero average) , else process converges against V 0!
Loop gain recovered while ‘smoother’ transients remain

## Slide 19
Smooth gain ramping technically difficult 
Possible to modify procedure: do not need device:
1)Smooth gain ramp 10.9
2) Measure r, calculate Sp(0.91)
3) Instant: Sp Sa, gain 0.91
1’)Smooth gain ramp 10.9
2’) Measure r, calculate Sp(0.91)
3’) Instant Sp Sa, gain 0.91
1”)Smooth gain ramp 10.9
2”) Measure r, calculate Sp(0.91)3”) Instant Sp Sa, gain=1
1”’) …
(Assume gain already at 0.9)
Measure r, calculate Sp(0.91)
2) Smoothly go from Sa to Sp as active S
1’) Measure r, calculate Sp(0.91)
2’) Smoothly go from Sa to Sp as active S
1”’) …
(no last ramping 0.9  1)
Jump gain 0.9 1
Smooth gain ramp 1  0.9
“Do nothing (but smooth)”

## Slide 20
Initial beam: Pg, Pr [0-400 kW], Vreal(Q), Vimag(I), | bunch position, | bunch energy
beam dump gap
Quadrature comp. of V (about constant)
Huge transients on Pg, Pr
89 µs = 1 LHC machine turn

## Slide 21
After smoothing (12 sec)
displaced bunch positions (full up-down scale: 50 ps) for nominal beam:
Small fraction of bunch length -> no problem for experiments
new Q-component of V
Nominal beam (only), ultimate scales with Ib
RF power is ‘flat’ and ‘low’: No transients anymore

## Slide 22
First measured transmitter Ig in LHC: Re[Ig] (I) Im[Ig] (Q)
10000 data, 3564 data/turn turn 1 2 3
© data from Ph. Baudrenghien, J. Molendijk

## Slide 23
Get some numbers: Use lumped circuit model
-> used quantities: (R/Q), Q0, Qext, Δω, Pg, Pr, Ib,DC, ϕ, Fb
(details see Appendix) V assumed real
real part
imaginary part
(R/Q)=V2/(2 ω Ust)
circuit Ω convention
ϕ = 0 for rising RF zero crossing (proton convention)

## Slide 24
J.T.: The Ultimate Beam in the 400 MHz RF system, CERN-ATS-Note-2010-038 TECH,
on http://cdsweb.cern.ch/
More than available: averaging over gaps helps (simulation)
Much more than available: irrecoverable -> need displaced bunches
Regular bunches:
Optimum settings Δf, Qext

## Slide 25
(ultimate) beam with perfectly displaced bunches:
(on paper) Pg=0(*) !!!! (with Qext  ∞)
Not a gag:
• No beam loading compensation required
• Cavity wall losses are zero (see (*)) for sc. cavity
• For Qext=∞ ‘zero’ power to keep up the field
In reality:
• Need enough power to push bunches back in case of
developing coupled bunch instability: ‘low’ Qext
• Qext=∞ means also Z=∞ : not possible, instabilities
• displacement and other parameter never perfect and
tend to drift in time (intensity loss by lumi, …)
e.g. with Qext=50-80k use P=150…250 kW (=const)
(*) the RF wall losses in the superconducting cavity are less than 50 W

## Slide 26
Summary
With the available 300 kW / cavity RF power and the present low-level beam control (no ‘smoother’) we can
 Capture nominal / ultimate(*) beam with reg. bunch distance
 Accelerate and coast(*) the nominal beam with reg. bun. dist.
But we cannot accelerate and coast the ultimate beam
With ‘smoother’ (or similar ?!?) we can
 Accelerate and coast ultimate beam with well pre-adjusted displaced bunches
(*) close to the limit of the hardware

## Slide 27
Thank you
for listening!
Notes: 27

## Slide 28
Appendix A:
The Fundamental Beam-Cavity-Generator Relations
Steady state currents and voltage: no transients considered.
(variable currents and voltages: Appendix B)
Lumped circuit model.
Cavity: LCR-block,
Coupler: transmission line with impedance Z
Beam: RF current source/sink: Ib.
Incident (generator) wave current: Ig
Reflected wave current: Ir (*)
Cavity is excited to voltage V.
(*) assumed to disappear without re-reflection (matched circulator with load)

## Slide 29
Fig. A1: the lumped circuit model: cavity modeled by LCR,
the coupler by a connected transmission line of impedance Z,
Beam by RF current source/sink Ib
For superconducting cavity R >>> Z (Q0 >>> Qext)

## Slide 30
Implicitly all dynamic variables are proportional exp(iωt).
Generator emits wave Ig with frequency ω :
Cavity tuned to ω0, (≠ω).
Transmission line
(A1)
(A2)
RF beam current Ib,RF ; ILCR through the LCR-block
(A3a) substituting (A2)
(A3b)
ILCR = the sum from parallel elements (steady state)
(A4)

## Slide 31
Combining (A4) and (A3b)
(A5)
LC = 1/ω02
(A6)
Δω = ω0 – ω << ω0
(A6)

## Slide 32
Cavity Quantity Dictionary
Carrying a charge q from one plate of a DC capacitor to the other one: voltage change
(A9)
Charge q travelling through a cavity with (R/Q): voltage
(A10)
(A11)
Any resonator has Q0=ωRC, apply (A11)
(A12) analog for Qext
(A13)
Convention: (R/Q) in circuit Ω (1 circuit Ω = 2 linac Ω)

## Slide 33
(A14)
Ib,RF is complex. We agree complex phase of all waves such that V is purely real.
Synchronous phase angle: angle of the RF voltage when the beam arrives. In electron machines ϕelec is called zero if beam and voltage are in phase.
V proportional to exp(iωt): the beam RF current proportional to exp(iωt – iϕelec).
In proton machines ϕ is zero at the rising zero crossing of the RF voltage, i.e. ϕ = ϕelec – 90º.
Using ϕ for the further calculations
(A15a)

## Slide 34
Complex Fourier spectrum of a ∞ repetitive charge passage
(point charges): equal line height (the DC current) for all frequencies from –∞ to +∞.
Corresponding real spectrum (no negative lines!):
equivalent positive and negative lines of complex spectrum exactly add up: 2x DC current amplitude … but
one unique line (zero-frequency) 1x DC current amplitude.
‘Point bunches’: any line f > 0 Ib,RF = 2 Ib,DC.
‘Longer’ bunches: lower than 2 Ib,DC (higher f lines).
Introduce relative bunch form factor Fb that is
normalized to 1 for infinitely short bunches.
(details: Appendix C)

## Slide 35
General case:
(A15b)
(A16)
(A17)
(A18)
Optimum reactive beam loading detuning: Im(Ig) = Im(Ir) = 0
(A19)
if superconducting
(A20) (Re(Ir) = 0)

## Slide 36
V(t)=A(t)·exp(iωt)
A(t): very small variation within an RF oscillation
<==> | dA2(t)/dt2 | << | ω2A(t) | (exploited later)
(B1)=(A3a)
(B2a)
(B2b)
(B2c)
Appendix B:
The Fundamental Beam-Cavity-Generator Relations
Variable amplitude for currents and voltage
with common carrier frequency ω
Use lumped circuit model of Appendix A

## Slide 37
Combining (B1) … (B2c)
(B3)
V(t) = A(t)exp(iωt) 
(B4)
Double partial integration:
(B5)
compared to ….. is negligible (‘slow A(t)’)

## Slide 38
Hence
(B6)
All variables proportional exp(iωt):
(B7)
(Check: For dA(t)/dt=0 reproduce (A5) as it should be.)
Introduce Δω=ω0-ω (as in Appendix A)
(B8)
Introduce cavity quantities (Appendix A)
(B9)

## Slide 39
Introduce beam current as in Appendix A
(B10)
and with (A2), (A13) (generally valid)
(B11)
General power formula
(B12)

## Slide 40
Appendix C: The Relative Bunch Form Factor Fb
Bunches cos2(x) charge distribution.
Bunch line density (normalized to 1)

## Slide 41
Relative bunch form factor Fb is the Fourier component :
Point bunch:

## Slide 42
Example for cos2-shaped bunches:
Bunch form factors Fb in LHC for 200, 400 and 800 MHz systems at injection (B=52 cm) and during coast (B=30cm)