## Slide 1: RF Power Sources and Related Issues
... and some non-related ...

## Slide 2: Outline
RF Power source issues (presented at Linac10 and IWLC10)
The RF activities inside EuCARD-NCLinac
The planned RF activities in TIARA
The planned RF activities in “HiLumi LHC” DS
A possible Network activity in EuCARD 2?

## Slide 3: RF Power Source Issues
Power — Efficiency — Complexity — Reliability — Cost

## Slide 4: The Need for Power
HEP:
  Future e+e− colliders (ILC, CLIC, …)
  Plasma-Wakefield accelerator (drive beam)
  Proton driver for Muon-collider, Neutrino-factory (Project-X, …)
Non-HEP:
  Spallation neutron sources, (SNS, ESS, …)
  Irradiation Facility (IFMIF, …)
  ADS

## Slide 5: The Need for Power
Many large future projects need large scale RF!
This is true for both average and peak powers.
 | IFMIF | ESS | SPL II | ILC .5 TeV | CLIC 3 TeV
Frequency | 175 MHz | 704 MHz | 704 MHz | 1300 MHz | 1000 MHz
Technology | Grid tubes | klystrons | klystrons | MBK | MBK
Total AC power |  | 38 MW | 40 MW | 230 MW | 415 MW
Modulator output | 60 MW | 17.8 MW | 26.5 MW | 135 MW | 255 MW
Power source output | 25 MW | 8.9 MW | 10.7 MW | 88 MW | 180 MW
Drive beam power |  |  |  |  | 140 MW
Acc. structure input | 15 MW | 6.5 MW | 7.8 MW | 67 MW | 101 MW
Total beam(s) power | 10 MW | 5 MW | 4 MW | 21.6 MW | 28 MW
Efficiency |  | 13.5 % | 10 % | 9.4 % | 6.7 %

## Slide 6: The Need for Efficiency
Overall AC to beam efficiency about 10%!
Increased efficiency would
  reduce the environmental impact,
  reduce the size of the installed power,
  reduce the size of the necessary cooling,
  decrease the electricity bill:
  Example:
CLIC @ 3 TeV, 415 MW AC consumption,
5,000 h operation per year, 40 $/MWh:
Annual electricity bill of 91 M$.
Assume that this is for a klystron efficiency of 65 %.
With a klystron efficiency increase by 1 % (66 %), you would save 1.4 M$ every year in electricity alone.

## Slide 7: Issue Complexity/Cost
Some of these projects cost ≈ 10 G$ or beyond.
RF sources may be important cost drivers (G$).
Clearly, when optimizing efficiency, one must not compromise on low cost. Solutions with potential easy mass production are preferred.
Large complexity will also complicate operation/maintenance.
For many small units, methods to implement graceful degradation may be implemented.

## Slide 8: Example of the State of the Art
Toshiba: E3736 (6 beam): 1.3 GHz, 10.4 MW, 10 Hz, 66 %, 49 dB gain
Thales: TH 1801 (7 beam): 1.3 GHz, 10.1 MW, 10 Hz, 63 %, 48 dB gain
CPI: VKL-8301B (6 beam): 1.3 GHz, 10.2 MW, 10 Hz, 66.3 %, 49.3 dB gain
1.
2.
3.

## Slide 9: Where to go from here?
The R&D for the ILC/X-FEL MBK’s was very successful.
However, the ideal power source may not be obtain from extrapolation of this concept.
Optimization is complex:
  more beamlets increase complexity and size,
  higher voltage will have impact on modulator
  higher current
... but it may pay off:

## Slide 10: Return on R&D Investment
Chart: peak power [MW]
| 0.15000000000000024 | 1.5 | 10 | 20 | 30 | 36
present state of the art | 0.4 | 0.17 | 0.1 | 0.1 | 0.115 | 0.128
Chart: peak power [MW]
| 0.15000000000000024 | 1.5 | 10 | 20 | 30 | 36
after dedicated R&D | 0.39 | 0.165 | 0.095 | 0.089 | 0.105 | 0.12

## Slide 11: Potential high η RF sources
Conventional (pencil beam) klystrons
Multi-beam klystrons MBK’s
Sheet beam klystrons (SBK)
Klystrons with MDC (multi-stage depressed collector)
IOT’s?
Magnetrons?
other – more exotic (Gyrocon?, ...)
Different methods of lost energy recovery (from RF, thermal, ...)

## Slide 12: The RF activities inside EuCARD-NCLinac

## Slide 13: RF related tasks in NCLinac:
High Gradient Cavities
  PETS
  HOM Damping
  Breakdown Simulation
  Precise Assembly
  Diagnostics
Stabilisation
Beam Delivery System
Drive Beam Phase Control
  Low impedance phase pick-up
  Bunch Arrival Time monitor

## Slide 14: NCLinac 9.2.1 PETS
Aim: design and build a double length PETS (Power Extraction and Transfer Structure) for CTF3
PETS STUDY

## Slide 15: NCLinac 9.2.1 PETS
Fabrication of the first copper rod by DMP (Spain) about to finish.
Two stress relieve treatments (2h @ 180ºC) performed to achieve the requested tolerances +/- 15 μm.
Dimensional control of the first copper rod to be carried out at DMP, using a fully automatic 3-D measurement machine.
Absorber material ordered.
Vacuum tank and vacuum ports will be made of stainless steel and TIG welded.

## Slide 16: NCLinac 9.2.2 HOM Damping
Aim: Design an alternative CLIC accelerating structure with manifold damping and strong detuning (DDS)
Cutaway-view
Prototype disc

## Slide 17: NCLinac 9.2.2 DDS
192 cells
8-fold interleaving
24 cells
No interleaving
192 cells
8-fold interleaving
Manifold
Coupling slot
∆fmin = 65 MHz
∆tmax =15.38 ns
∆s = 4.61 m
∆fmin = 8.12 MHz
∆tmax =123 ns
∆s = 36.92 m
∆f=3.6 σ
=2.3 GHz
∆f/fc=13.75%
Meets
design
Criterion?

## Slide 18: NCLinac 9.2.3 BD Simulation
Aim: Simulate breakdown phenomena to help understand the physics
DFT: Density Functional Theory
MD: Molecular Dynamics
ED: Electrodynamics
KMC: Kinetic Monte-Carlo
PIC: Particle In Cell

## Slide 19: NCLinac 9.2.3 BD Simulation
SEM photo
Simulation

## Slide 20: NCLinac 9.5: Phase control
Aim: Design PU to detect phase of CLIC drive beam to better than 20 fs precision

## Slide 21: NCLinac 9.5.1: Low Z Phase PU
RF noise
RF noise
reflected
reflected
12 GHz
notch
filter
12 GHz
notch
filter
Beam signal
pick-up
Beam induced signal
beam
12 GHz resonating volume

## Slide 22: NCLinac 9.5.2: BAM
BAM: Bunch Arrival Monitor

## Slide 23: The planned RF activities in TIARA
Test Infrastructure and Accelerator Research Area
http://www.eu-tiara.eu/

## Slide 24: TIARA-pp Goals and Partners
Objectives:
The main objective of TIARA (Test Infrastructure and Accelerator Research Area) is the integration of national and international accelerator R&D infrastructures into a single distributed European accelerator R&D facility.
This will include the implementation of organisational structures to enable the integration of existing individual infrastructures, their efficient operation and upgrades, and the construction of new infrastructures as part of TIARA.
TIARA will enable full exploitation of the complementary features and expertise of the individual member infrastructures, maximizing the benefits for both the owners of these infrastructures and their users.
This unique distributed facility will also support the development of an integrated R&D programme embracing the needs of many different fields, as well as medical and industrial sectors, both on technical and human resource aspects.
Besides a world-level state-of-the-art distributed R&D facility, TIARA will develop means for establishing and supporting joint accelerator R&D programming, joint education and training programmes and strengthened collaboration with industry.
Partners:
CEA ,CERN, CNRS, CIEMAT, DESY, GSI, INFN, PSI, STFC, UU, IFJ-PAN

## Slide 25: TIARA-pp Work Packages
Management (CEA)
Governance (CEA)
R&D Infrastructures (CERN)
Joint R&D Programming (INFN)
Education and Training (STFC)
Small Vertical Emittance Tuning (CERN)
Ionisation Cooling Test Facility (STFC)
High Gradient Acceleration (INFN)
Test Infrastructure for High Power Accelerator Components (CNRS)

## Slide 26: RF activities in TIARA
In WP7, a Diacrode® based, pulsed 200 MHz, 2...3 MW amplifier for a MICE upgrade (ICTF) will be studied (Task 7.3).
WP8, High Gradient Acceleration, will design C-band accelerating structures for a SPARC energy upgrade to 200MeV (Tasks 8.1 & 8.3) and a digital LLRF system (Task 8.2).

## Slide 27: The planned RF activities in HiLumi LHC DS
LHC Crab Cavities:

## Slide 28: HiLumi LHC DS
HL-LHC is a major CERN recognized project and has a scope of enabling LHC to attain in 10-12 years (about 2020 - 2030) an integrated luminosity of 3 ab-1!
  All hadron colliders of the World have produced so far about 10 fb-1 in total; LHC will deliver in its first 10-12 years (hopefully) about 200-300 fb-1.
HiLumi LHC is the “Design Study” part of HL-LHC, the FP7 proposal was sent 25-Nov-2010 to Brussels.

## Slide 29: HiLumi LHC Work Packages
Management & Coordination
Accelerator Physics and Performance
Magnet Design
Crab Cavities
IR Collimation
Cold Powering
HiLumi LHC WP4 will build on the success of EuCARD WP10.3 and RFTech.
More details: Talk by Rama Calaga this morning

## Slide 30: A possible Network activity in EuCARD 2?
Back to my initial subject “High efficiency, high power RF sources”

## Slide 31: EuCARD 2 (?)
EuCARD 2 (working name) is in the planning phase (2011 call) ...
UU and others identified the need for “Sustainable and energy efficient RF”; I have suggested to include a Network Activity focused on “High Efficiency RF Power Generation”.
This Network would connect people interested in the field and working on “waste less power” in RF power generation.
Initial reaction was very positive.
... à suivre ...

## Slide 32: Thank you very much!