## Slide 1: Minimizing the field tilts in superconductive cavities
Results from 2011 ILC tests at FLASH, DESY
Julien Branlard
RFTech, 3rd Workshop
Rostock, Dec. 12th 2011

## Slide 2: Overview
Problem statement and historical background
  Why do we care about individual flat gradients?
  What solutions were offered to achieve flat gradients with beam loading?
  What can we actually implement at FLASH?
The Feb.’11 study at FLASH
  What approach have we followed during the FLASH test studies?
  Results of the PK |QL studies
Conclusions and prospects
  Approach limitations
  Improvements

## Slide 3: I. Introduction: ILC
The International Linear Collider
Accel. Params | ILC | FLASH | Unit
Cavity tech. | SC | SC | 
RF freq. | 1.3 | 1.3 | GHz
Rep. rate | 5 | 5-10 | Hz
Beam current | 9 | 1-9 | mA
Average gradient | 31.5 | 26 | MV/m
RF station | 10 MW klystron for 26 cavities | 10 MW klystron for 16 cavities | 

## Slide 4: I. Introduction: FLASH
FLASH
ACC67

## Slide 5: I. Introduction: problem statement
Why do we care about individual flat gradients?
  “Effect of Cavity Tilt and RF Fluctuations to Transverse Beam Orbit Change in ILC Main Linac” K. Kubo, Jan. 2010
Beam loading
BEAM OFF
BEAM ON

## Slide 6: I. Introduction: problem statement
Beam loading tilts scale linearly with beam current
  Simulated tilts for ACC6 at FLASH, with 800 usec flat top
Chart: Beam current [ mA ]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
ACC6.1 | -0.2 | 0.68 | 1.6 | 2.48 | 3.36 | 4.24 | 5.12 | 6.04 | 6.92 | 7.79
ACC6.2 | -0.09 | 1.02 | 2.18 | 3.29 | 4.4 | 5.52 | 6.63 | 7.79 | 8.9 | 10.01
ACC6.3 | 0.06 | 0.71 | 1.39 | 2.04 | 2.7 | 3.35 | 4 | 4.68 | 5.33 | 5.98
ACC6.4 | -0.04 | 0.49 | 1.04 | 1.57 | 2.1 | 2.63 | 3.16 | 3.72 | 4.25 | 4.78
ACC6.5 | 0.06 | -3.4 | -7.02 | -10.48 | -13.94 | -17.41 | -20.87 | -24.49 | -27.95 | -31.42
ACC6.6 | -0.04 | -3.19 | -6.48 | -9.64 | -12.79 | -15.94 | -19.09 | -22.38 | -25.53 | -28.68
ACC6.7 | 0.01 | -1.21 | -2.5 | -3.72 | -4.95 | -6.17 | -7.4 | -8.68 | -9.9 | -11.13
ACC6.8 | -0.04 | -1.35 | -2.73 | -4.04 | -5.35 | -6.66 | -7.98 | -9.35 | -10.66 | -11.97

## Slide 7: I. Introduction: problem statement
“Solutions” to flat cavity gradient with beam
  “RF Distribution Optimization in the Main Linacs of the ILC”, Bane, Adolphsen, Nantista – PAC07
  “Optimal Coupler and Power Settings for Superconductive Linear Accelerators”, Branlard, Chase - LINAC08
  “PkQl-like control for ACC6/7 at FLASH”, Michizono, unpublished 2010
“RF Distribution Optimization in the Main Linacs of the ILC” Bane, Adolphsen, Nantista - WEPMS037.pdf, 2007
     Assumes a square forward power pulse
     Assumes adjustable PK’s

## Slide 8: I. Introduction: problem statement – FLASH working space
Focus on ACC6 and ACC7
Motorized couplers (QL adjustments, limited range)
Fixed power distribution (i.e. PK), except for 3dB hybrid
Motorized slow tuners
Dynamic cavity resonance control with piezo

## Slide 9: II. Analytical approach
Analytical ‘solution’ for optimal QL
 assumes “perfect” tuning
 solve for QLi when possible
cavity i loaded Q
cavity i forward power during fill time [W]
DC beam current [A]
fill time ( beam arrival time) [s]
fill time to flat top voltage ratio (including beam compensation)

## Slide 10: II. SIMCAV: Cavity simulator

## Slide 11: II. SIMCAV: Cavity simulator

## Slide 12: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
DAQ data: Feb. 07 2011, 22:37
Ib = 4.5 mA
FLASH DAQ data
Notes: How did we proceed to flatten individual cavity gradients: knobs we used are: adjusting QLs and setting cavity on resonance
Step 1: load DAQ data, decay measurement

## Slide 13: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
simulated data
vector sum
Notes: Step 2: simulate

## Slide 14: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
FLASH DAQ data
simulated data
vector sum
Notes: Check agreement between simulation and experimental data

## Slide 15: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
simulated data
vector sum
Notes: Adjust QL using simulator “by eye”

## Slide 16: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
simulated data
vector sum
Notes: Adjust QL using simulator “by eye”

## Slide 17: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
simulated data
vector sum
Notes: Note that while adjusting the QL flattens cavity gradients during beam time, it also introduces a tilt when beam is OFF

## Slide 18: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
FLASH DAQ data
simulated data
vector sum
Notes: Verify benefits (in tilts) of the Ql change (retune cavity after QL adjustments)

## Slide 19: II. Calibration procedure
Load Vcav from DAQ
Compute actual QL , PK and f from DAQ data
Type in QL, PK and f into simulator
Check agreement between simulated and FLASH data
Adjust QL in simulator to flatten tilts
Implement QL corrections in FLASH
Check gradient flatness
FLASH DAQ data
simulated data
vector sum
Notes: Close up on simulation vs. experiment data: discrepancies are due to:
Inaccuracy in assessing power distribution
Inaccuracy in the Ql estimate “by eye”
Inaccuracy in setting up the Ql (settings + measurement)
Inaccuracy in cavity tuning (static + dynamic)

## Slide 20: II. Assessing the accuracy of the method
QL scan
   Keep beam current constant but walk QL’s around optimized value
IB scan
   Keep optimized QL’s but ramp beam up/down
-0.6 -0.4 - 0.2 0 0.2 0.4 0.6 0.8
QL [ x 106 ]
3
2
1
0
-1
-2
-3
gradient tilts [%]
Notes: Checking if the Ql settings are indeed optimal

## Slide 21: II. Assessing the accuracy of the method
QL scan
   Keep beam current constant but walk QL’s around optimized value
IB scan
   Keep optimized QL but ramp beam up/down
Notes: Checking the impact of beam change on tilts (Qls are optimized for 1 beam current, not any other beam current)

## Slide 22: II. Assessing the accuracy of the method
QL settings are limited
ILC specs : 9 mA !

## Slide 23: II. Impact of cavity frequency tuning
Before freq. tuner adjustments
After freq. tuner adjustments
AMPLITUDE
AMPLITUDE
PHASE
PHASE
~ 0.1 MV/m
QL = 1.58x106
QL = 1.58x106
f = 70 Hz

## Slide 24: III. Study insights
What went well
Motorized couplers / tuners
Analytical approach proved to be useful
Predicted optimized QL values were accurate  to 0.2e6
Successfully implemented the tuning plan  tilts < 0.1MV/m
What we’ve learnt
Cavity resonance control is crucial for gradient tilts
Limitations to the analytical approach:
  How accurately can we compensate for LFD OR include in model?
  How accurately can we measure and set QL’s  +/- 2 to 5%
What is still unanswered
No proposed solution for high beam currents (>6mA) implementable at FLASH
There is not always a solution to flatten all cavities (especially when gradient spread is large)
No solution to bring up the machine at its highest gradient

## Slide 25: III. Conclusions and prospects
Machine automation
  Automatic QL settings
  Automatic quench detection
Machine operation scenarios
  Tuning strategies
  How to ramp up the beam
  How to recover from a quench
Next study time
  February 2012
Thank You!