## Slide 1
Ultracold neutron production at the second spallation target of the Paul Scherrer Institute
Bernhard Lauss
Paul Scherrer Institute
on behalf of the PSI UCN Project Team
Paul Scherrer Institute
Villigen, Switzerland

## Slide 2: Contents
- Introduction to the PSI ultracold neutron source
- How we make the D2 crystal
- UCN measurements and specific tests

## Slide 3
Neutron production via proton spallation on lead
UCN Source
Proton Accelerator
590 MeV Cyclotron
2.2 mA beam current
2.4 mA regular test operation days
nEDM
installed
2 experimental areas / 3 beamlines
kicker to UCN

## Slide 4
Sketch of the PSI UCN source
pulsed 1.3 MW p-beam
590 MeV, 2.2 mA,
1% duty cycle
spallation target (Pb/Zr)
(~ 8 neutrons/proton)
heavy water moderator
→ thermal neutrons
3.6m3 D2O
cold UCN-converter
~30 dm3 solid D2 at 5 K
tank
7 m
DLC coated
UCN storage vessel
height 2.5 m, ~ 2 m3
UCN guides towards
experimental areas
8.6m(S) / 6.9m(W)
SV-shutter
cryo-pump

## Slide 5: The lead spallation target
756
Zr/Pb
Canneloni
length = 390 cm weigth = 2000 kg cooling = 10 kg D2O / sec
Pb
Fe
AlMg3 Container
Steel shielding
Beam window
Target array
Pb structure
p

## Slide 6
M. Wohlmuther, G. Heidenreich / Nuclear Instruments and Methods in Physics Research A 564 (2006) 51–56
first MCNP-X simualtions
Initial neutron yield ~7 n per primary proton
Now technical details of the spallation target,
lead-block versus cannelloni type target,
and more accurate model (as built).
-> total cold n flux ~ factor 2 lower than in original estimate
MCNPX calculations by
Vadim Talanov,
Michael Wohlmuther
1016p/s

## Slide 7
Activation measurement
- gold foil activation measurement
- first full Monte Carlo Simulation and measurement agree at beam height within 30%. (15% uncertainty from foil position)
- tritium activation measurement, development of new method, first analysis ongoing
MCNPX calculations update underway (Michael Wohlmuther, Vadim Talanov)

## Slide 8
Beam operation scheme
800s
8s
1% duty cycle
full proton beam up to 2.4 mA
tested operation of pulses from 7ms, 50ms to 8s
and beam currents from 100 to 2400 mA
continuous mode operation possible with beam current <20 mA

## Slide 9
Beam operation scheme
800s
8s
1% duty cycle
full proton beam up to 2.4 mA
tested operation of pulses from 7ms, 50ms to 8s
and beam currents from 100 to 2400 mA
continuous mode operation possible with beam current <20 mA

## Slide 10
- D2O purity checked in Jan 2012 - good as expected
Heavy water system for
neutron moderation and target cooling
delay column

## Slide 11
UCN Tank

## Slide 12: UCN storage volume
1 m
DLC coating
vertical
UCN guide
2 - 6 mm thick
ultrapure Al

## Slide 13
Installation of the storage volume unit and the deuterium unit
fall 2010
10 tons
steel
vertical UCN guide
2 - 6 mm thick
ultrapure Al
thermal shield 70K (surrounding the storage volume)
~5m
←±15mm
main shutter
cryo pump

## Slide 14: Neutron guides pass the biological shield and guide the UCN to the experimental areas
glass parts
-ID=180mm
surface roughness better than 1nm
coated with NiMo
~8 m length from storage volume to experiment port passing through the shield
>98% UCN transmission per meter measured for all guide parts
- sample for every guide measured with cold n reflectometer ~ 217 neV
- every installed guide was tested with UCN at PF2,
cordial thanks to Peter Geltenbort and Thomas Brenner
nEDM

## Slide 15
Installation of longest UCN guide towards nEDM
nEDM thermohouse

## Slide 16
Check conversion of Ortho-to Para-Deuterium
rotational Raman peaks
S0(0)
S0(1)
S0(2)
S0(3)
S0(4)
 98 ± 2 % ortho-D2
reconfirmed in several measurements
ortho/para fraction
UCN lifetime in D2 (ms)
30
20
10
LANL /
C.Morris et al,
Phys.Rev.Lett.89(2002)272501
at 98% ortho-D2 tucn dominated by: Nuclear absorption s(H) =0.3barn s(D)=0.0005barn

## Slide 17
30m3
Preparation of the deuterium crystal
slow condensation
He-refrigerator cooling power: 370W @4.2K
and 2500W @ 80K
slow transfer

## Slide 18
cool-down:
para-ortho conversion
(using Oxisorb)
20 K
Preparation of the deuterium crystal
D2 Transfer ~1% / hour

## Slide 19: Solid deuterium at 5K
200 mm
2 × 1.5 mm AlMg4.5Mn
0.5 mm AlMg3
500 mm
Cooling Agent: Supercritical Helium

## Slide 20
100
200 mm
0.5 mm AlMg3
500 mm
Cooling Agent:
Supercritical Helium
D2
- solid/liquid/gas level
- lid transmission
saturated vapor pressure indicates
D2 temperature
D2
2 × 1.5 mm AlMg4.5Mn
Solid deuterium at 5K

## Slide 21
warming up
Triple-Point
all D2 is liquid
start cooling
Triple-Point
solid
full cooling to final pressure
Vapor pressure for crystal #2012-2
this example:
7 hours at triple-point,
tried up to 24 hours
mbar
Pa

## Slide 22
- Construction and commissioning of the source was completed in 2010
- Federal authorities` operation approval obtained in June 2011
- Start-up with first beam August 3, 2011 - up to PSI shutdown Dec.2011
- Full operation in 2012 with nEDM data taking up to winter shutdown
Operations History

## Slide 23
Measurement in area West
with detector at beam-port
pilot
pulse
filling
storage
vessel
emptying
storage
vessel
>2x107 UCN /pulse
ZOOM
closing
shutter

## Slide 24
best normpulse performance in 2010: 30,000 2011: 2,020,000 2012: 2,600,000
Compare UCN intensity over time - normpulses
-no mechanical shutter movement
preliminary

## Slide 25
only 50% differences in UCN output
with crystal growing times between
30min and 2days
Characterization of D2 crystals
best normpulse performance in 2010: 30,000 2011: 2,020,000 2012: 2,600,000
record high with 2.4mA
2012
2011
super
fast
surface
liquefaction
>15Pa
first fill from
tanks
take out
50 mbar
UCN per normpulse
preliminary

## Slide 26
A benchmark: UCN density
VAT
Cascade
Detector
VAT
1m glass tube ~25000 cm3 comparable to nEDM precession chamber ~2100 cm3
- NiMo coating
- Stainless
steel flanges
- shutter DLC coated
UCN
UCN density measured in a 25l volume
extrapolated to t=0
at PSI area West-1
2010 ~0.15 UCN/cm3
2011 ~18 UCN/cm3
2012 ~23 UCN/cm3
=> correct for detector foil transmission
present status >33 UCN/cm3 in storage experiment
preliminary

## Slide 27
A benchmark: UCN density
VAT
Cascade
Detector
VAT
1m glass tube ~25000 cm3
- nEDM precession chamber ~2100cm3
- NiMo coating
- Stainless
steel flanges
- shutter DLC coated
UCN
UCN density measured in a 25l volume
extrapolated to t=0
at PSI area West-1
2010 ~0.15 UCN/cm3
2011 ~18 UCN/cm3
2012 ~23 UCN/cm3
=> correct for detector foil transmission
present status >33 UCN/cm3 in storage experiment
preliminary
One could imagine to do common measurements of densities in the same bottle at different UCN sources to compare source performances.

## Slide 28
UCN Ping Pong
Test of guides and storage vessel
detector
2
superconducting magnet
as polarizer
detector
1
- kick beam onto target
- fill small storage vessel in West-1
- open source storage vessel shutter after 10 s
- UCN stored in West-1 for 100s - can be directly measured
- open W1 storage vessel shutter - towards W1 -> measure
- open W1 storage vessel shutter - towards South -> send UCN from West to South
- measure UCN arriving in South
negligible Background

## Slide 29
full simulation reproduces measurements well (~30%)
 no 'big' unknowns in storage vessel or guides
UCN transmission
from West to South
measured = 2.9 ± 0.4%
simulated = 3.3 ± 0.3%
UCN Counts / pulse
UCN Ping Pong tests
guides and storage vessel
preliminary

## Slide 30
Moderator lid UCN transmission
- use lid material from pressure test vessel
- 50% transmission of 0.5mm thick AlMg3 as expected from previous measurements of the material finally used
holder with 2 samples

## Slide 31: UCN Storage Time via leak method
preliminary

## Slide 32
Deuterium Crystal Conditioning
2012: very good Temperature control
up to 2 days at Triple Point

## Slide 33
D2 gas measurements
[can potentially provide an unambiguous calibration]
Simulation: energy dependent neutron flux (MCNPX) and UCN transport.
Calculate from first principles energy dependent UCN production on individul D2 molecules and loss cross sections, compare to published measurements from FUNSPIN
0.5s proton kick
D2 gas moderator
work in progress
Simulation of neutron flux:
calculate UCN production:
simulate UCN extraction and transport through full system to detector.
compare!
verification by experiment done or under way
UCN counts
prompt background

## Slide 34
- The components of the UCN source are commissioned and operating well.
- We are exploring the different parameters necessary in crystal freezing.
- PSI UCN source has regular beam operation to supply UCN to the nEDM apparatus and other users.
- UCN density improved by factor of 80 since start-up. Still about 15 times below design. Further optimization of all source parameters is under way
Summary

## Slide 35
Thanks for your attention
the Paul Scherrer Institute
UCN source
location