## Slide 1: TLEP: A first step in a long-term vision for HEP
TLEP Design Study : 2013 - 2018
  Supported by CERN strategy, in the context of a global project
    See Design Study Proposal at http://tlep.web.cern.ch/
    Most recent workshop 4-5 April 2013 (CERN)
      https://indico.cern.ch/conferenceDisplay.py?ovw=True&confId=240814
    Next workshops : 25-26 July 2013 (FNAL) and 16-18 October 2013 (CERN)
      https://indico.cern.ch/conferenceDisplay.py?confId=246137 Register !
    Design Study kick-off workshop in December 2013 or January 2014
CERN implementation
A. Blondel
J. Osborne and C. Waajjer

## Slide 2: TLEP: A first step in a long-term vision for HEP
Recommendations from European Strategy Group
  High-priority large-scale scientific activities
    Recommendation #2
    Excerpt from the CERN Council deliberation document (22-Mar-2013)
d) To stay at the forefront of particle physics, Europe needs to be in a position to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update, when physics results from the LHC running at 14 TeV will be available.
CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.
The two most promising lines of development towards the new high energy frontier after the LHC are proton-proton and electron-positron colliders. Focused design studies are required in both fields, together with vigorous accelerator R&D supported by adequate resources and driven by collaborations involving CERN and national institutes, universities and laboratories worldwide. The Compact Linear Collider (CLIC) is an electron-positron
machine based on a novel two-beam acceleration technique, which could, in stages, reach a centre-of-mass energy up to 3 TeV. A Conceptual Design Report for CLIC has already been prepared. Possible proton-proton machines of higher energy than the LHC include HE-LHC, roughly doubling the centre-of-mass energy in the present tunnel, and V-LHC, aimed at reaching up to 100 TeV in a new circular 80km tunnel. A large tunnel such as this could also host a circular electron-positron machine (TLEP) reaching energies up to 350 GeV with high luminosity.

## Slide 3: A compendium of misconceptions about TLEP
Heard repeatedly
  TLEP is more expensive than the ILC
  TLEP parameters are stretched by many-order-of-magnitude extrapolations
  TLEP will come later than ILC
  TLEP is superfluous once ILC is approved and starts construction
  TLEP will delay VHE-LHC
  TLEP RF power is unacceptable (600 MW?!)
  TLEP physics case is the same as that of ILC (at low energy)
  TLEP can only do Higgs couplings / TLEP does not cover the physics case
    We need a machine upgradeable beyond 350 GeV to make discoveries beyond LHC
  TLEP precision is an overkill
    Higgs couplings do not need to be measured so precisely
All are wrong
  With the upgrade path to a 100 TeV machine (unique to TLEP)
    TLEP is the first step in a long-term vision for particle physics
      And might be the only way to secure high-energy physics in Europe

## Slide 4: Scientific Motivation (1)
A new boson with mass ~ 126 GeV, and with SMS properties
  Example : H(126) → ZZ → 4 leptons in CMS and ATLAS
    H(126) couples to the Z boson : important for e+e- colliders
      gHZZ compatible with SM prediction (within ±30%)
      Scalar hypothesis favoured
      mH known to ~ 400 MeV
      sHZ largest at √s = 250 GeV
Moriond EW ’13

## Slide 5: Scientific Motivation (2)
Today’s situation
  A (very) Standard Higgs boson
    Very strong motivation to measure all couplings with high precision
      What precision ?
J. Ellis et al.

## Slide 6: Scientific Motivation (3)
No sign of new physics below a scale of several 100’s GeV
  Supersymmetry (ATLAS) Exotics (CMS)
  Data at higher √s will extend the coverage to ~500 GeV for SUSY
    Will know in 2017 : might need to look for (multi-)TeV New Physics
      Air is getting very thin for Linear Colliders with √s = o(TeV)
        We need a machine upgradeable beyond several TeV
Moriond EW ’13

## Slide 7: Scientific Motivation (4)
If no new physics is found, what next ?
  Once mH is known, the standard model has nowhere to go !
    Very strong incentive to revisit and improve all precision measurements
      Z pole, WW threshold
      Higgs couplings
      Top quark properties
      Rare decays (Bs → mm, etc.)
    With the precision needed to become sensitive to (multi-)TeV New Physics
→ Programme unique to TLEP
→ Also at the Z pole, unique to TLEP
→ Integrated luminosity unique to TLEP
R. Kogler et al.
LHCb 2013
→ Integrated luminosity unique to TLEP

## Slide 8: Scientific Motivation (5)
Example : Precision for Higgs couplings
  Maximal deviations with respect to SM couplings, as a function of new physics scale
    SUSY , for tanb = 5
    Composite Higgs
    Top partners
    Other models may give up to 5% deviations with respect to the Standard Model
  Maximal deviations for the new physics scale still allowed by LHC results
Strongly influences the strategy for Higgs factory projects
  Need at least a per-cent accuracy on couplings for a 5s “observation”
    And sub-percent precision if new physics is at the (multi-)TeV scale
H. Baer, M. Peskin et al.
J.D. Wells et al.

## Slide 9: Precision at existing colliders : (HL-)LHC (1)
Executive summary
Approved LHC, 300 fb-1 at 14 TeV :
  Higgs mass at 100 MeV
  Disentangle Spin 0 vs Spin 2 and main CP component in gg/ZZ*
  Coupling precision / Experiment
    ZZ, WW, 5-6%
    bb, tt 10-15%
    tt, mm 3-2 s effect
    gg , gg 5-11%
HL-LHC, 3000 fb-1 at 14 TeV:
  Higgs mass at 50 MeV
  More precise studies of Higgs CP sector
  Coupling precision / Experiment
    ZZ, ZW, 1-5%
    bb, tt, tt, mm 3-10%
    gg and gg 2-7%
    HH >3 s (2 Expts)
Assuming sizeable reduction of theory errors
CMS (#177) and ATLAS (#174) contributions to the European Strategy (2012)

## Slide 10: Precision at existing colliders : HL-LHC (2)
Graphic representation of HL-LHC projected performance
  Much better than originally expected before LHC started
    Will need vigorous upgrade of CMS and ATLAS detectors
      Per-cent to sub-percent precision will require new collider(s)
?
?
?
Assumptions :
No new decay
SM corr. for BR(cc) )
In bold, theory uncertainty are assumed to be divided by a factor 2,
experimental uncertainties are assumed to scale with 1/√L,
and analysis performance are assumed to be identical as today
[11]
ATLAS upper limit at 65%
(Moriond EW 2013)
From CMS (#177) contribution to the European Strategy (2012)

## Slide 11: P0ssible paths towards the future
Several options for Higgs factories are being studied
This talk
(mostly TLEP)
Not encouraged by
European Strategy
Smaller Physics
Potential
Studied for decades
e+e- colliders have largest potential
as Precision Higgs Factories

## Slide 12: The Visionary Solution : TLEP + VHE-LHC (Worst case solution : LEP3+HE-LHC)
Build a new 80-100 km circular tunnel :
  TLEP Physics case : Precision measurements sensitive to multi-TeV New Physics
    TeraZ (√s~mZ), MegaW (√s~2mW), Higgs Factory (√s~240 GeV), top (√s~350 GeV)
      With luminosity 5-1000 × larger than projects of similar timescale and cost
  Followed by VHE-LHC : Direct search for New Physics in the 10-100 TeV range
    √s ~ 100 TeV with 20T magnets
      Also allows the HHH coupling to be measured to a few %
PSB
PS (0.6 km)
SPS (6.9 km)
LHC (26.7 km)
TLEP : e+e-, up to
√s ~350 GeV
VHE-LHC : pp,
√s ~ 100 TeV
LEP3 : e+e-, up to
√s ~ 240 GeV
HE-LHC (33 TeV)
(CERN implementation)
F. Zimmermann

## Slide 13
«Pre-Feasibility Study for an 80-km tunnel at CERN»
John Osborne and Caroline Waaijer,
CERN, ARUP & GADZ, submitted to ESPG
80-km tunnel in Geneva area – “best” option
even better
100 km?

## Slide 14: Luminosity at TLEP (1)
Luminosity increases when √s decreases at circular colliders
  By optimal use of the RF power to collide more bunches when SR decreases (1/E4)
  Ultimate precision measurements are therefore made possible at circular colliders
    Crossing point with linear colliders ~ 450 GeV
      Luminosity upgrade (×3) now envisioned at ILC : luminosity is the key !
TLEP : Instantaneous lumi at each IP (for 4 IP’s)
Z, 2.1036
WW, 6.1035
HZ, 2.1035
tt , 5.1034
R. Aleksan
√s (GeV) | # Bunches
91 | 4000
240 | 80
350 | 12
With LHeC-inspired
optics/parameter

## Slide 15: Luminosity at TLEP (2)
Luminosity achieved by reducing the vertical b*
  From 5 cm (LEP2) to < 1 mm (TLEP)
    Note : 0.3 mm soon to be realized at SuperKEKB
  Vertical beam size < 200 nm
    Note : 1 to 5 nm for Linear Colliders
      Hence negligible Beamstrahlung for Physics, beam energy well known
 | TLEP-H | TLEP-t | ILC (250) | ILC (350)
beam energy [GeV] | 120 | 175 | 125 | 175
disruption Dy | 2.2 | 1.5 | 23.4 | 84.5
ϒBS [10−4] | 15 | 15 | 207 | 310
nγ/collision | 0.50 | 0.51 | 1.17 | 1.24
DdBS/collision [MeV] | 42 | 61 | 1265 | 2670
DdBSrms/collision [MeV] | 65 | 95 | 1338 | 2760
F. Zimmermann

## Slide 16: Luminosity at TLEP (3)
At these luminosities, beam lifetime ~ 15 minutes (Bhabha scattering)
  Solution : double ring and continuous top-up injection, as at PEP-II
    Note : Soon to be realized at Super-KEKB, beam lifetime ~ 5 minutes
        Top-up injection : Schematic cycle
        (Provisional logo)
        Contest to be organized !
A. Blondel
TLEP
F. Zimmermann
M. Koratzinos

## Slide 17: Challenges (A subset)
Beamstrahlung
  Radiating e± pushed outside the acceptance
    Reduces the beam lifetime significantly
  Need to design an achromatic optics at the IPs
    with 2-3% momentum acceptance
Efficient RF system
  Need 12 GeV/turn at 350 GeV
    ~900 m of SC RF cavities @ 20 MV/m
      LEP2 had 850 m at 7 MV/m
  Very high power : up to 200 kW / cavity in the collider ring
    Power couplers similar to ESS – 700-800 MHz preferred
Small vertical emittance
  Can/should further reduce beamstrahlung by minimizing sy/sx
    Aim is to reach 0.1% (LEP2 had 2%, SuperKEKB plans 0.2%)
Operation at the Z pole
  4000 bunches : e+ source, impedance effects, parasitic collisions
    May need two rings designed to separate e+ and e- beams
BNL 5-cell 700 MHz cavity
M. Zanetti
RF Coupler
(ESS/SPL)

## Slide 18: “TLEP RF Power is unacceptable (600 MW?!)”
RF parameters and total power consumption at 350 GeV
  RF Parameters : TLEP RF ~ LHeC RF
  Total Power Consumption (MW)
  F. LeDiberder : 55% should be 17% (like ILC)
    LEP2 already reached 42%
    CLIC Drive Beam foresees 55%
    CEBAF enjoys 55%
      Difference between CW and Pulsed
 | LHeC | TLEP collider | TLEP inj.
beam energy [GeV] | 60 | 175 | 175
frequency [MHz] | 720 or 800 |  | 
total voltage [GV] | 20 | 12 | 9
av gradient [MV/m] | 20 | 20 | 20
eff. RF length [km] | 1 | 0.6 | 0.6
#cavities | 1000 | 600 | 600
Efficiency (wall→beam) | 55% | 55% | 55%
power throughput [MW] | 17 | 110 | 10 (peak)
power / cavity [kW] | 17 | 183 | 17
 | TLEP
Wall-plug RF power | 181
RF cryo power | 24
Magnet system power | 6
Cooling and ventilation | 60
Experiments | 25
General services | 15
SPS & PS as pre-injectors | 5
e-/e+ source & pre-pre-injector | 1
Total | 318
E. Jensen, A. Butterworh, F. Zimmermann, M. Koratzinos

## Slide 19: “TLEP parameters are stretched by huge extrapolations”
Extrapolation from past experience
        Example : beam size @ IP
  SuperKEKB will be an excellent test-bench for TLEP
    In many respects
  Will also learn a lot from ATF2
  Lot of work ahead to reach ILC beam dimensions
  Estimates for circular colliders historically reliable
 | LEP2→TLEP-H | SLC→ILC 250
peak luminosity | × 400 | × 2500
energy | × 1.15 | × 2.5
vertical geom. emittance | × 1/5 | × 1/400
vert. IP beam size | × 1/15 | × 1/150
e+ production rate | × 1/2 ! | × 65
commissioning time | <1 year → ? | >10 years →?
LEP2 | 3500
KEKB | 940
SLC | 500
LEP3 | 320
TLEP-H | 220
ATF2, FFTB | 72, 65
SuperKEKB | 50
SAPPHiRE | 18
ILC | 5 – 8
CLIC | 1 – 2
F. Zimmermann

## Slide 20: “TLEP is more expensive than the ILC (1)”

## Slide 21: “TLEP is more expensive than the ILC (2)”
Very rough estimate (Giga-CHF)
ILC cost (2012 re-evaluation) : 7.8 Giga-$
  Many items not included
    Site construction, infrastructure engineering, detectors, coming R&D, …
Bare tunnel | 3.1 (1)
Services & Additional infrastructure (electricity, cooling, service cavern, RP, ventilation, access roads …) | 1.0(2)
RF system | 1.0 (3)
Cryo system | 0.2 (4)
Vacuum system & RP | 0.5(5)
Magnet system for collider & injector ring | 0.8(6)
Pre-injector complex SPS reinforcements | 0.5
Total | 7.1
Note: detector costs not included – can count 0.5 per detector (CMS/ATLAS)
(1): J. Osborne, Amrup study
(2): Extrapolation from LEP
(3): B. Rimmer, SRF cost per GeV or
per Watt for CEBAF upgrade, 2010
O. Brunner, complete evaluation, 2013
(4): F. Haug, 4th TLEP Days, 5 April 2013
(5): K. Oide : factor 2.5 higher than KEK,
estimated for 80 km ring
(6): 24,000 magnets for collider & injector;
cost per magnet 30 kCHF (LHeC);
10% added; no cost saving from mass
production assumed
preliminary – not endorsed by anybody

## Slide 22: TLEP Physics case as a Higgs Factory (1)
Physics case not driven by the fact that the collider is linear or circular
  Scan of the HZ threshold : √s = 210-240 GeV Spin
  Maximum of the HZ cross section : √s = 240-250 GeV Mass, sHZ, BRs, Width, Decays
  Just below or at the tt threshold : √s ~ 340-350 GeV Width
Z → nn
Z → All
Unpolarized cross sections
[7]
Need 100’s fb-1
PJ and G. Ganis

## Slide 23: TLEP Physics case as a Higgs Factory (2)
A few specificities, though :
  e- (e+) beam polarization is easy at the source (possible) for a linear collider.
    Not critical for Higgs studies.
  No beam disruption from Beamstrahlung for a circular collider (sy ~ 300 nm vs. 5 nm @ ILC)
    No EM backgrounds in the detector (photons, e+e- pairs);
    No beam energy smearing – energy spectrum perfectly known (lumi measurement)
    Negligible pile-up from gg interactions
      No drastic requirements for the detector and the background simulation
  Possibility of operating several IP’s simultaneously in circular collider
    vs. only one IP in linear collider
ILD TPC at 500 GeV
M. Zanetti
ILD LoI

## Slide 24: TLEP Physics case as a Higgs Factory (3)
Number of Higgs bosons produced at √s = 240-250 GeV
  In a given amount of time, Higgs coupling precisions scale like
    e.g., for gHZZ : 1.5% for ILC : 0.65% for LEP3 : 0.2% for TLEP
      Five years of TLEP = 75-150 years of ILC (at 240 GeV)
    Note : measure total Higgs boson width GH
      At 240 GeV : With sHZ (~ g2HZZ) and sHZ × BR(H→ ZZ) (~ g4HZZ/GH)
      At 350 GeV : With sWW→H (~ g2HWW) and sHZ × BR(H→ WW) (~ g2HZZg2HWW/GH)
 | ILC-250 | LEP3-240 | TLEP-240
Lumi / IP / 5 years | 250 fb-1 | 500 fb-1 | 2.5 ab-1
# IP | 1 | 2 - 4 | 2 - 4
Lumi / 5 years | 250 fb-1 | 1 - 2 ab-1 | 5 - 10 ab-1
Beam Polarization | 80%, 30% | – | –
L0.01 (beamstrahlung) | 86% | 100% | 100%
Number of Higgs | 70,000 | 400,000 | 2,000,000
Upgradeable to | ILC 1TeV CLIC 3 TeV ? | HE-LHC 33 TeV | VHE-LHC 100 TeV

## Slide 25: Higgs measurements at √s ~ 240 GeV (1)
With e+e- → ZH → e+e-X and m+m-X events
  Measure HZ cross section in a model independent way
    Find mH peak from the leptons and E,p conservation
    Determine spin with three-point threshold scan
      10 fb-1 / point suffice
    Determine sHZ and gHZZ coupling at 240 GeV
      3% (1.5%) precision on sHZ (gHZZ)with 250 fb-1
    Good tracker needed, but details mildly depend on the actual performance
      Plots below with ILD@ILC and CMS@TLEP
e+
e-
Z*
Z
H
e+, m+
e-, m-
e+e- → ZH → e+e-X and m+m-X
e+e- → ZH → m+m-X
Dp/p ~ 0.2%
Dp/p ~ 2%
[9,10,11]
e+e- → ZH → m+m-X
    gHZZ
P. Azzi et al.
ILC TDR

## Slide 26: Higgs measurements at √s ~ 240 GeV (2)
With ZH → e+e-X and m+m-X events (cont’d)
  Measure invisible decay branching ratio (X = nothing)
    Precision on BRINV ~ 1% with 250 fb-1
    Or exclude BRINV > ~2% at 95% C.L.
Measure other sHZ×BR(H→ ff,VV)
  With exclusive selections of Z and H decays
    Precision of 1.5% to 8% with 250 fb-1 for the copious decays (bb, WW, gg, tt, cc)
    Need more luminosity for rare decays (gg, Zg, mm)
      Particle flow, b and c tagging, lepton and photon capabilities needed
ZH→ qqbb, 250 fb-1 ZH→ llWW→ lllnqq, 500 fb-1 ZH→ Xgg, 500 fb-1 ZH→ Xmm, 2 ab-1
P. Azzi et al.
H. Baer et al.

## Slide 27: Higgs measurements at √s ~ 240 GeV (3)
Higgs width from the ZZZ final state
  Number of ZZZ events ~ sHZ × BR(H→ ZZ)
    sHZ ~ g2HZZ
    BR(H→ZZ) = GH→ZZ/GH ~ g2HZZ / GH
      Number of ZZZ events ~ g4HZZ / GH
  Select l+l- l’+l’- X events ( ~ background and H →WW free)
    Number of events in 250 fb-1 @ 240 GeV :
      250 fb-1 × 200 fb × BR(H→ZZ) × BR(Z→ll)2 × 3
        → About 40 events, of which ~25 selected
  Hence measure the total width GH with a precision of 21% with 250 fb-1
    Could be further reduced with other Z decays
e+
e-
Z*
Z
H
Z*
Z
Known to 6%
from l+l-X events
with 250 fb-1

## Slide 28: Higgs measurements at √s ~ 240 GeV (4)
Higgs width from the Hnn final state
  From sWW→H and BR(H→ WW)
    sWW→H ~ g2HWW
    BR(H→ WW) = GH→WW / GH ~ g2HWW / GH
      GH ~ sWW→H / BR(H→ WW)
  Contribution to Hnn from HZ ~ 40 pb
    Known from ZH → e+e-X and m+m-X
  Contribution from WW fusion ~ 6 pb
    To be measured
  Select nnbb events from ZH and WW fusion
    Needs adequate b tagging and particle flow
  Fit the missing mass distribution for NWW→H→bb
    sHZ x BR(H→ bb) known to ~1.5% or better
    sWW→H = NWW→H→bb / BR(H→ bb)
      Precision on sWW→H ~ 14% with 250 fb-1
      GH ~ sWW→H / BR(H→ WW), measured up to 15% precision with 250 fb-1
    gHWW
C.F. Duerig, LCWS’12

## Slide 29: Higgs measurements at √s ~ 240 GeV (5)
Precision on H(125) branching fractions, width, mass, … after 5 years
  LEP3 numbers obtained from a CMS simulation x 4, except (*) extrapolated from ILC
    Need a refined vertex detector for gg and cc BR accurate measurements
  TLEP numbers extrapolated from LEP3 column – ILC numbers with super-duper ILC detector
 | ILC | LEP3 (4) | TLEP (4)
sHZ | 2.5% | 1.3% | 0.4%
sHZ ✕BR(H→bb) | 1.0% | 0.5% | 0.1%
sHZ ✕BR(H→cc) | 6.9% | 4% (*) | 1.3%
sHZ ✕BR(H→gg) | 8.5% | 4.5% (*) | 1.4%
sHZ ✕BR(H→WW*) | 8.0% | 3.0% | 0.9%
sHZ ✕BR(H→tt) | 5.0% | 3.0% | 0.9%
sHZ ✕BR(H→ZZ*) | 28% | 7.1% | 3.1%
sHZ ✕BR(H→gg) | 27% | 6.8% | 3.0%
sHZ ✕BR(H→mm) | – | 28% | 13%
sWW→H | 11% | 5% (*) | 2.2%
GH , GINV | 10% , < 1.5% | 4% , < 0.7% | 1.8% , < 0.3%
mH | 40 MeV | 26 MeV | 8 MeV
HF2012 Worskshop

## Slide 30: Higgs Measurements at √s ~ 350 GeV
Luminosity for TLEP ~ 5 x ILC @ 350 GeV
  At each IP : 500 fb-1 over 5 years
    With possibly 4 detectors at TLEP
  More study of the Hnn final state with H→bb
    Contribution from HZ : ~ 25 fb
    Contribution from WW→H : ~ 25 fb
      Improves precision on GH and HWW coupling
      Smaller improvement (by ~20%) of all other s✕BR measurements
 | ILC (250+350) | TLEP (240+350)
sWW→H | 12% → 3% | 2.2% → 0.5%
GH | 10% → 5.5% | 1.8% → 1.1%
C.F. Duerig, LCWS’12
ILC TDR, June 2013 (to appear)

## Slide 31: TLEP Physics case as a Higgs Factory (4)
Summary of the ICFA Higgs Factory Workshop (FNAL, Nov. 2012)
Best
precision

## Slide 32: TLEP Physics case as a Higgs Factory (5)
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      ILC250 would complement LHC (esp. for GH , Ginv , gHcc , gHbb)

## Slide 33: TLEP Physics case as a Higgs Factory (5)
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      ILC250/350 would further complement LHC, but does not cover the physics case

## Slide 34: TLEP Physics case as a Higgs Factory (5)
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      LEP3 would be an advantageous back-up : larger lumi, several IPs, smaller cost

## Slide 35: TLEP Physics case as a Higgs Factory (5)
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      TLEP would be a superior option (see zoom next page)
See zoom
Next page

## Slide 36: TLEP Physics case as a Higgs Factory (6)
Need sub-percent precision for a sensitivity to multi-TEV New Physics
  Total width fixed to the sum of the visible partial widths + correction
    Summary : TLEP reaches the needed accuracy
      ILC prospects similar to HL-LHC’s
    Much theoretical work also needed
HF2012
J. Ellis et al.

## Slide 37: TLEP Physics case as a Higgs Factory (7)
A slide from M. Peskin at the 3rd TLEP/LEP3 Worskshop (10-Jan-2013)

## Slide 38: TLEP Physics case as a Higgs Factory (8)
Same conclusion when GH (measured) is a free parameter in the fit
  Plot shown only for ILC350 and TLEP, with an accurate width measurement
      TLEP : sub-percent precision, adequate for NP sensitivity beyond 1 TeV
M. Peskin’s fit

## Slide 39: Top Measurements at √s ~ 350 GeV (1)
Scan of the tt threshold
  Observables stt, AFB and <p@max> sensitive to mtop , Gtop , and ltop (ttH Yukawa coupling)
    Experimental precision (for ILC, 300 fb-1)
      No beamstrahlung and luminosity x 4 at TLEP
    Expected sensitivity for TLEP with 500 fb-1 /IP in five years (full study to be done)
    Studies of rare top decays
 | Dmtop | DGtop | Dltop/ltop
TLEP | 15 MeV | 17 MeV | 15%
ILC | 30 MeV | 35 MeV | 40%
stt
p@max
AFB
mtop = 175 GeV
M. Martinez and R. Miquel, 2003

## Slide 40: Top Measurements at √s ~ 350 GeV (1)
Scan of the tt threshold
  Observables stt, AFB and <p@max> sensitive to mtop , Gtop , and ltop (ttH Yukawa coupling)
    Experimental precision (for ILC, 300 fb-1)
      No beamstrahlung and luminosity x 4 at TLEP
    Expected sensitivity for TLEP with 500 fb-1 /IP in five years (full study to be done)
    Studies of rare top decays
DGt = 200 MeV
stt
p@max
AFB
M. Martinez and R. Miquel, 2003
Dlt/lt = 0.25
DGt = 200 MeV
 | Dmtop | DGtop | Dltop/ltop
TLEP | 15 MeV | 17 MeV | 15%
ILC | 30 MeV | 35 MeV | 40%

## Slide 41: Physics case of the energy upgrades (1)
All existing proposals have access to larger √s
  To discover New Physics in a direct manner (beyond the scope of this talk)
  To measure more difficult Higgs couplings : gHtt and gHHH
    ILC350 can be upgraded to ILC500/ILC1TeV, or even to CLIC (3 TeV) [?]
    LEP3 can be upgraded to (or preceded by) HE-LHC (33 TeV)
    TLEP can be upgraded to VHE-LHC (100 TeV)
H
H
Cross sections in pp collisions
Cross sections in e+e- collisions
M. Mangano

## Slide 42
VHE-LHC + TLEP
L. Rossi
multipurpose tunnel
HE-LHC
(20 T)
HE-LHC-LER (0.17→1.5 T)
TLEP collider (0.07 or 0.05T)
TLEP injector (0.007→0.05/7 T)
20 mm thick shield around cable
Gaps: 2 x V30xH60 mm
transmission line magnet
(B. Foster, H. Piekarz)
super-resistive cable

## Slide 43: Physics case of the energy upgrades (2)
Summary for Htt and HHH couplings
  Other Higgs couplings benefit only marginally from high energy
    TLEP + VHE-LHC looks like a winning team
√s, NP
√s, NP
ILC500, HL-LHC ILC1TeV, HE-LHC CLIC3TeV, VHE-LHC
(NP=New Physics reach)
HF2012

## Slide 44: Measurements at smaller √s (1)
Revisit and improve the LEP precision measurements
  TLEP can do the entire LEP1 physics programme in 5 minutes
  Important : Polarization up to the WW threshold with TLEP
    Very precise beam energy determination (10 keV) : unique to circular colliders
      Measure mZ, GZ to < 0.1 MeV, mW to < 1 MeV, sin2θW to 2.10-6 from ALR
 | LEP | ILC | LEP3 | TLEP
√s ~ mZ | Mega-Z | Giga-Z | ~Tera-Z | Tera-Z
Lumi (cm-2s-1) #Z / year Polarization vs LEP1 | Few 1031 2x107 no 1 | Few 1033 Few 109 easy ~5-10 | Few 1035 Few 1011 yes (T, L) ~50 | 1036 1012 yes (T,L) ~100
√s ~ 2mW |  |  |  | ¼ Oku-W
Lumi (cm-2s-1) Lumi / IP / year Error on mW | Few 1031 10 pb-1 220 MeV | Few 1033 50 fb-1 7 MeV | 5x1034 500 fb-1 o.7 MeV | 1.5x1035 1.5 ab-1 0.5 MeV
√s ~ 200-250 GeV |  |  |  | Oku-W
Lumi (cm-2s-1) Lumi / IP / 5 years Error on mW | 1032 500 pb-1 33 MeV | 5x1033 250 fb-1 3 MeV | 1034 500 fb-1 1 MeV | 5x1034 2.5 ab-1 0.5 MeV
Asymmetries, Lineshape
WW threshold

## Slide 45: Measurements at smaller √s (2)
Case 1 : Only SM physics in EW Radiative Corrections – Stringent SM Closure test
  Set stringent limits on weakly interacting new physics (mH, mW and mtop known)
    Much theoretical work also needed
Case 2 : Some weakly interacting new physics in the loops ?
  Will cause inconsistency between the various observables
    Become sensitive to multi-TeV WINP
      LEP1 was sensitive to ~ 200 GeV (mtop)
+
mW
?
Linear
(ILC)
Circular
(LEP3)
mH = 126 GeV
Circular
(TLEP)
M. Grunewald

## Slide 46: Measurements at smaller √s (3)
Experimental challenges are numerous : TLEP(Z)
  At TLEP(Z), the hadronic Z event rate will be 15 kHz
    Rate of bunch crossings similar to that at LHC (400o bunches over 80 km)
    CMS current high-level trigger rate is about 1 kHz
      (But hadronic Z events typically 20 times smaller than typical LHC event)
    Need to design a detector and a DAQ system able to cope with these rates
      A clever mixture of LHC detector (rate) and ILC detector (precision)
        Need to study what is the precision needed for each sub-detectors
        Is a CMS-like detector sufficient ? (~OK for Higgs studies)
  Small angle Bhabha event rate (lumi measurement) will be even larger : 60 kHz
    Essential to measure cross sections, hence the Z lineshape (mZ, Gz)
      Negligible beamstrahlung is a great advantage
        No background in the luminometers
        Energy spectrum perfectly known (hence Bhabha cross section)
      Will need theoretical developments to understand se+e- to better than 5 x 10-5
  Limiting uncertainties on aQED(mZ) and as(mZ) must be overcome
    Possible with the billions of e+e- → e+e-(g) , m+m-(g) and qq(g) events ?
      Will affect all Z peak asymmetries, and mZ vs mW interpretation
-
PJ, A. Blondel
Nn

## Slide 47: Measurements at smaller √s (4)
Experimental challenges are numerous : TLEP(Z)
  Z lineshape needs a precise beam energy measurement
    Resonant depolarization unique @ circular machines
      Intrinsic precision ~ 100 keV (LEP1) / measurement
        Decreases like 1 / √#(Measurements)
    Requires beam transverse polarization
      In one non-colliding bunch, during operations
        Continuous energy measurement
        No extrapolation needed (tides, trains, rain…)
    Will require installation of polarization wigglers
      Natural polarization time ~ 150 h at TLEP …
        But only 15h for 10% polarization…
  Polarized asymmetry (ALR) requires longitudinal polarization
    Hence spin rotators and polarimeters at each IP
      Then need to keep polarization in collisions
        That’s the main unknown
        Dedicated operations with lower luminosity ?
    Dedicated study is needed here

## Slide 48: Measurements at smaller √s (5)
Experimental challenges are numerous : mW at TLEP(W) and TLEP(H)
  With 1.5 ab-1 at TLEP(W) and 6. 106 WW events/expt at threshold : s(mW) ~ 0.5 MeV
  With 2.5 ab-1 at TLEP(H), 4x107 W pairs/expt : s(mW) ~ 0.2 MeV
  Need to know beam energy to a fraction of MeV
    Use the precision Z mass measurement from the Z pole
      With 3x107 Z(g) events (Z  e+e-, m+m-) / expt at TLEP(W)
      With 2x106 Z pairs and 5x106 Z(g) events (Z  e+e-, m+m-) / expt at TLEP(H)
        Can reach combined statistical precision on Ebeam of 0.3 MeV and 0.4 MeV
  Beam transverse polarization possible at TLEP(W) : precision better than 0.1 MeV
  Need to understand both theoretical and experimental uncertainties…

## Slide 49: Possible Timescale
Similar timescales for TLEP and LEP3
TLEP
  Design study : 2013-2017
  Next European Strategy Workshop : 2017-2018
  Decision to go and start digging : 2018-2019
  Start installation in parallel with HL-LHC running : 2023 - …
  Start running at the end of HL-LHC running : 2030 - …
LEP3
  Design study : 2013-2017 (spin-off of TLEP design study)
  Next European Strategy Workshop : 2017-2018
  Decision to go : 2018-2019
  Start installation at the end of LHC running : 2022 - …
    Tunnel probably irradiated at the end of HL-LHC
      LEP3 is an alternative of HL-LHC, and could be followed by HE-LHC in 2040
  Start running when ready : 2027 - …
 | 2010 |  |  |  |  |  | 2015 |  |  |  |  | 2020 |  |  |  |  | 2025 |  |  |  |  | 2030 |  |  |  |  | 2035 |  |  |  |  | 2040
LHC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HL-LHC | R&D + constr |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TLEP* |  |  |  | Design + R&D + construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
VHE-LHC* | Design + R&D + construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 50: “TLEP is more expensive than the ILC”
LEP3 : A cost-effective option
  Tunnel : 0 $ - Cryoplant : 0$
  Two detectors : 0$ - Four detectors : 1 G$ Total : 1 – 2 G$
  RF + Magnets + Injector Ring : 1 G$
  100,000 Higgs boson / detector / 5 years @ 240 GeV : 5 k$ / Higgs boson
TLEP : A long-term vision
  Tunnel : 4 G$
  Four detectors : 2 G$ Total : 9 G$
  RF + Cryo + Magnet + Injector Ring : 3 G$
  500,000 Higgs boson / detector / 5 years @ 240 GeV : < 4.5 k$ / Higgs boson
Comparison with ILC
  Total Cost : > 10 G$
  70,000 Higgs boson / 5 years @ 240 GeV
of which 5 G$ in common
with SHE-LHC
> 150 k$ / Higgs boson

## Slide 51: Design Study : 2013 – 2018 (1)
F. Zimmermann
ad interim
P. Janot
ad interim
J. Ellis
ad interim
R. Aleksan, A. Blondel, J. Ellis, P. Janot, M. Koratzinos, M. Zanetti, F. Zimmermann ad interim

## Slide 52: Design Study : 2013 – 2018 (2)
Experimental Studies : Preliminary Structure (Being discussed)
  11 working groups
    WG1 : Electroweak Physics at the Z pole
    WG2 : Di-boson physics : W mass measurement, …
    WG3 : H(126) properties
    WG4 : Top Quark Physics
    WG5 : b, c and t physics
    WG6 : QCD and gg physics
    WG7 : Rare Physics
    WG8 : Experimental environment
    WG9 : Offline software and computing
    WG10 : Online software and computing
    WG11 : Detector designs

## Slide 53: Conclusions
We believe TLEP to be the best complementary machine to LHC
  Higgs properties precision measurements; Stringent test of the SM closure.
TLEP is based on a well-known technology
  Supported by much progress in e+e- circular factories for 20 years (and counting)
    LEP, LEP2, (super) b factories, synchrotron light sources
  Based on this experience, luminosity, power and cost predictions will be reliable
It is a first step in a long-term vision for high-energy physics
  Many synergies with VHE-LHC (pp collisions at 100 TeV)
    Tunnel, accelerator, experiments, physics
The design study is starting up as we speak, supported by CERN strategy
  Join us at http://tlep.web.cern.ch/contribute-to-the-design-study
    196 people registered as of today, 10:30am, … and counting
The goal is to have a technically-ready proposal by 2018
  So that the community can take a fully-informed decision
    with the LHC Run2 results at √s = 13-14 TeV in hand
We aim for physics in 2030

## Slide 54
?!?
?!?
Free the donkeys!
F. LeDiberder
Revu par R. Aleksan