## Slide 1: GBAR Gravitational Behaviour of Antihydrogen at Rest
Motivation
Principle of the experiment
Experimental technique
Perspectives
Measurement of the free fall of antihydrogen atoms

## Slide 2: MOTIVATION
A direct test of the Equivalence Principle with antimatter:
The acceleration imparted to a body by a gravitational field is independent of the nature of the body :
Inertial mass = gravitational mass

## Slide 3: Gravitation and cosmology
Matter-antimatter asymmetry in the Universe ???
Is there a repulsive antimatter-matter interaction ???
A. Benoît-Lévy, G. Chardin A&A 537 (2012) A78
No quantum theory of gravitation
  new theories may contain additional interaction terms different for matter and antimatter

## Slide 4: Experimental limits
Limits on gravitational acceleration (call it g ) for antimatter:
Arrival time of one (? : 90 % CL) neutrino and 18 antineutrinos from SN1987a
S. Paksava et al. Phys Rev D 39 (1989) 1761
CPLEAR: CP violation in K0-K0 as a function of time depends on m A. Apostolakis et al., Phys Lett B 452 (1999) 425
Cyclotron frequency measurement of
p (H-) and p in the same B field
G. Gabrielse et al. Phys Rev Lett 82 (1999) 3198
Alpha: location of annihilation of antihydrogen atoms
Nature Comm 4, 1785 (2013)

## Slide 5: GBAR principle: cool H+ to get ultra-slow H
Produce first H+
Capture H+ in trap
Cooling with Be+
→ 10 µK
Photodetachment of excess e+
Time of flight
h = 1/2 g (t1-t0)2
H+
gravity
detector (t1)
detector
Laser (t0)
H in free-fall
J.Walz & T. Hänsch,
General Relativity and Gravitation, 36 (2004) 561.
Cooling 10 µK
H+ = p e+e+
Uncertainty dominated by temperature of H +

## Slide 6: Why antihydrogen ?
Charged antiparticles (e+ or p):
gravity force on e+ ~ force from 1 e- at 5 m !
Antineutrons:
difficult to slow down and keep enough
Positronium (e+e- ):
lifetime, cooling, ionisation
project by D. Cassidy

## Slide 7: H+ production
p | + | Ps | → | H | + | e –
H | + | Ps | → | H+ | + | e –
closed geometry to keep density
(SiO2 reflects Ps)
Dump ~1010 e+ in Ps converter
in < τPs=142 ns
e+ trap
accumulate ~ 2 1010 e+
every p burst ~ 2’
Linac
3 108 slow e+/s
Yield of o-Ps :~ 30-40 %
p
_
1- 6 keV
e + ~ 3 keV
P
s
H
_
+
SiO2 coating
o
H
_

## Slide 8: Yield of o-Ps : 30-40 % !
Measurement
at CERN
Measurement
at UCR
~ 5.6 x 1016 e+ cm-2s-1
~ 3.5 x 105 e+ cm-2s-1
No loss in conversion efficiency in spite of the 1011 intensity factor
e+ flux
x
~1011
L.Liszkay et al., Appl. Phys. Lett. 92 (2008) 063114
D. B. Cassidy et al., Phys. Rev. A 81 012715 (2011)

## Slide 9: A possibility to enhance H+ production
P. Comini and P.-A. Hervieux, New Journal of Physics 15 (2013) 095022

## Slide 10: Overall GBAR scheme

## Slide 11: Overall GBAR scheme

## Slide 12: Future installation at CERN

## Slide 13: p decelerator
CSNSM Orsay

## Slide 14: Overall GBAR scheme

## Slide 15: e+/Ps demonstrator at Saclay
e- LINAC :
4.3 MeV / 200 Hz / 2.5 μs / 120 μA
3 106 slow e+/s
with W mesh moderator
Penning trap on beam line
from RIKEN
First e+ accumulation trials
Ps* laser being prepared at LKB (Paris)

## Slide 16: RIKEN Multi-Ring Trap

## Slide 17: New e+ trapping mechanism
e- density 1017 m-3 → e+ cooling time 3 ms

## Slide 18: First e+ accumulation
Thèse de P. Grandemange, Université Paris-Sud, 12 décembre 2013

## Slide 19: Overall GBAR scheme

## Slide 20: Two Cooling Steps
> 10 000 laser cooled Be+ ions
100 neV, T ~ mK
few mm
300 eV, T = 240 000 K
First step
T
÷ 3 109
Capture and sympathetic Doppler cooling by laser cooled positive ions
313 nm laser
in a linear capture trap (Paul trap, r0 = 3.5 mm, W = 13 MHz)
Second step
Transfer and ground state cooling ~ 10 µK
of a Be+/H+ ion pair in the precision trap
Mainz
H+
Tests with a H2+ / H+ REMPI source

## Slide 21: Two Cooling Steps Sympathetic Doppler cooling
L. Hilico, J-P. Karr, A. Douillet, P. Indelicato, S. Wolf, F. Schmidt-Kaler, to be published in IJMPCS

## Slide 22: Two Cooling Steps Sympathetic Doppler cooling
L. Hilico, J-P. Karr, A. Douillet, P. Indelicato, S. Wolf, F. Schmidt-Kaler, to be published in IJMPCS

## Slide 23: Two Cooling Steps Ground state cooling
L. Hilico, J-P. Karr, A. Douillet, P. Indelicato, S. Wolf, F. Schmidt-Kaler, to be published in IJMPCS
Ground state sympathetic cooling
of a Be+/H+ ion pair

## Slide 24: Overall GBAR scheme

## Slide 25: H free fall detection
H+
Aim : measure g to
1 % precision (first phase)
~ 1500 events needed

## Slide 26: Perspective : Velocity selector
G. Dufour, P. Debu, A. Lambrecht, V. Nesvizhevsky, S. Reynaud, A. Voronin Eur. Phys. J. C 74 (2014) 2731
Reflection probability
Idea : keep only atoms with a small initial vertical velocity
The gain in precision outweighs the loss in statistics
See G. Dufour’s talk

## Slide 27: Spectroscopy of gravitational states
H source:
  very low temperature
  high phase-space density
  compact system
Improve the precision on g with the spectroscopy of gravitational levels of H above the annihilation plane: similar method as for UCN neutrons
(GRANIT spectrometer)
A. Yu. Voronin, P. Froelich, and V. V. Nesvizhevsky, Phys. Rev. A 83, 032903 (2011)
See A. Yu. Voronin talk

## Slide 28: 15 institutes ~ 50 researchers 2015 start installation 2016 ELENA commissioning with p & H- 2017 first antiprotons for GBAR
SPSC-P-342, Proposal to measure the Gravitational Behaviour of Antihydrogen at Rest, GBAR, CERN (2011)